## Slide 1
CHALLENGE B
What Is Unsafe in This Picture?
Hazard Identification Challenge B · Pre-start vehicle check
Notes: Welcome. This challenge is about the pre-start check: deciding whether a vehicle is safe to drive BEFORE you set off. Ask: Who checks the dashboard every time they start a vehicle? What do you do if a light stays on?

## Slide 2: What Is Unsafe in This Picture?
You start a pool car. These lights stay ON after the engine starts.
Find the 5 lights that mean: DO NOT DRIVE
Notes: Set the scene: you start a pool car and these lights stay ON after the engine starts. Ask: Which 5 lights mean you must NOT drive until the vehicle is checked? Call out the numbers. Expected answers (keep hidden): 57 oil pressure, 48 engine temperature, 40 brake system, 39 airbag, 52 bonnet open. Give the group 60–90 seconds.

## Slide 3: Need a Clue?
1
Clue 1: Colour
Red usually means a serious warning.
2
Clue 2: Driving
What could fail while you are moving?
3
Clue 3: Protection
What protects you, or could block your view?
Other lights are also on. Some are safe information lights, others need attention soon.
Notes: Only use these clues if the group is stuck. Reveal them one at a time. Clue 1: red usually means a serious warning. Clue 2: what could fail while you are driving (engine, brakes)? Clue 3: what protects you in a crash, and what could block your view? After the clues, collect the group's answers before revealing.

## Slide 4: Answers: The 5 Do-Not-Drive Warnings
1
Oil pressure low
2
Bonnet open
3
Engine overheating
4
Airbag (SRS) fault
5
Brake system fault
Notes: Click once per answer. 1 #57 Oil pressure low: the engine can seize. 2 #52 Bonnet open: it can fly up and block the view. 3 #48 Engine temperature: the engine is overheating. 4 #39 Airbag (SRS): airbags may not deploy. 5 #40 Brake system: parking brake on, low fluid or a brake fault. Also mention: #51 door open and #59 boot open must be closed before moving. #49 ABS and #62 engine light need prompt inspection.

## Slide 5: Why It Matters: Engine and Brakes
1
Oil pressure low (#57)
Why it's dangerous
The engine can seize and stop suddenly in traffic.
What to do
Do not drive. Check the oil level and report it.
3
Engine overheating (#48)
Why it's dangerous
Engine damage, breakdown, and burns from hot coolant.
What to do
Do not drive. Let it cool; never open a hot cap.
5
Brake system (#40)
Why it's dangerous
Brakes may fail, or the parking brake may be dragging.
What to do
Release the parking brake. If the light stays on, do not drive.
Notes: Reveal one card per click. For each one ask: What could happen if you drove anyway? Oil pressure and overheating: stop the engine to prevent serious damage. Brakes: never drive with a brake system warning that stays on.

## Slide 6: Why It Matters: Protection and Visibility
2
Bonnet open (#52)
Why it's dangerous
The bonnet can fly up at speed and block your view.
What to do
Close it fully and check it is latched.
4
Airbag fault (#39)
Why it's dangerous
Airbags may not deploy in a crash.
What to do
Report it; get it repaired before use.
Pre-start rule
A red warning that stays on after start-up = do not drive.
Tag the vehicle and report it.
Notes: Reveal one card per click. Airbag: the vehicle should not be used until it is repaired (follow company policy). Bonnet: a bonnet that flies open at speed blocks the whole windscreen. Remind the group: if in doubt, don't drive; report it to your supervisor.

## Slide 7: Which Hazard Is the Most Serious?
A
Oil pressure low
B
Bonnet open
C
Engine overheating
D
Airbag fault
E
Brake system
Trainer's view: E, the brake system. Losing braking can cause a collision instantly. A (oil pressure) and C (overheating) can also stop the engine without warning. All five mean: do not drive.
Notes: Ask everyone to vote with their hands: A, B, C, D or E. Ask two people to explain their choice. Then click to show the trainer's answer. There is no single 'right' answer. The brake system (E) can cause a collision immediately. Oil pressure and overheating can stop the engine without warning. All five mean: do not drive.

## Slide 8: Key Learning Points
1
Look
Check every light after start-up: most should go out in a few seconds.
2
Decide
Red light still on? Do not drive. Amber? Get it checked soon.
3
Report
Tag the vehicle and tell your supervisor. Never hand over a faulty car.
Notes: Recap the three steps of a pre-start check. Ask: what will you do the next time a red light stays on after start-up?