## Slide 1
Plan
Verify
Authorise
Communicate
Monitor
Close
MODULE 7 · HSE TRAINING
Permit to Work (PTW)
A beginner-friendly course for Gas Treatment plant teams
Based on: Module 7 Course Notes – Permit to Work (Review 10 Feb 26)
Notes: TRAINER EXPLANATION: Welcome everyone. Today we learn the Permit to Work system – PTW for short. It is the system we use to control non-routine, high-risk work in our gas plant. You do not need any previous PTW experience. We will build up step by step: what PTW is, why we need it, the types of permits, who does what, how a permit moves from request to closure, and what to do when things change. SIMPLE EXAMPLE: Think about the jobs we do in a gas treatment plant: opening a flange, replacing a pump seal, entering a vessel, welding a pipe support. Each of these can release gas, fire, energy or toxic H2S if it is not controlled. PTW is how we control them. ASK THE TRAINEES: Who here has already worked under a permit? What do you remember about it? EXPECTED ANSWER: Accept any answers – this tells you the experience level of the group. TRAINER REMINDER: Everything in this course comes from the approved Module 7 Course Notes. Tell trainees that site-specific procedures always apply on site. SOURCE: Module 7 Course Notes – Section 1.0 Overview

## Slide 2: Your Learning Journey Today
SECTION 1
What is PTW & why?
SECTION 2
Principles & Life Saving Rule
SECTION 3
Types of permits
SECTION 4
Roles & responsibilities
SECTION 5
The PTW process
SECTION 6
Risk assessment
SECTION 7
Permit conditions & isolation
SECTION 8
Gas testing
SECTION 9
PPE & emergencies
SECTION 10
During the work
SECTION 11
Extension, cancellation & closure
SECTION 12
Records, audits & competence
SECTION 13
Scenarios & key takeaways
Notes: TRAINER EXPLANATION: This is the map for today. We start with the basics – what PTW is and why it exists – and finish with real plant scenarios. Each section builds on the one before, so do not worry if a word is new: we explain every technical term when it first appears. TRAINER REMINDER: Point out that Section 13 (scenarios) is where trainees will apply everything. Encourage questions at any time – asking questions is exactly what PTW wants people to do. SOURCE: Module 7 Course Notes – Table of Contents, Sections 1.0–14.0 (reorganised for beginners)

## Slide 3: Learning Objectives
By the end of this course you will be able to:
Explain what a Permit to Work is and why it exists
Know when a permit is required – and the Life Saving Rule
Recognise the main permit types and their key controls
Describe who does what: Issuer, Receiver and other roles
Follow the PTW lifecycle from request to closure
Understand isolation (LOTO), gas testing and emergency planning
Know when to STOP work and what happens next
Learn · Ask · Apply
Notes: TRAINER EXPLANATION: These are the seven things you should be able to do at the end of today. Notice the last one: knowing when to stop work. Every person on site has that right and that duty – including the newest trainee. ASK THE TRAINEES: Which of these objectives do you think is the most important for your own safety? EXPECTED ANSWER: Any answer is fine. Most trainees choose 'know when to STOP work' or 'understand isolation' – use this to connect to their daily work. TRAINER REMINDER: These objectives match the General Awareness and PTW User training outcomes in the Course Notes: people must know what the system is, why it exists, and how to work safely within a permit. SOURCE: Module 7 Course Notes – Sections 1.1.3 and 12.1.2 (Tier 1 & Tier 2 outcomes)

## Slide 4
SECTION 1
What is a Permit to Work – and why do we need it?
The basics: definition, purpose and what can go wrong
Notes: TRAINER EXPLANATION: In this first section we answer two simple questions: what is a permit, and why do we bother with one? SOURCE: Module 7 Course Notes – Sections 1.1 and 1.2

## Slide 5: What is a Permit to Work?
A formal, written safety process for planning, reviewing, authorising and controlling work
Used for non-routine work with significant risk
A written dialogue between the people who own the workplace and the people who do the work
Forces a “Time Out for Safety” before any tool is lifted or any valve is turned
Creates a “safe envelope” inside which high-risk work can be done
Permit Issuer
Owns the workplace / equipment (e.g. Operations Shift Supervisor)
THE PERMIT
Permit Receiver
Does the work (e.g. Maintenance Supervisor / Foreman)
Purpose: protect people, assets, the environment and the plant’s operational integrity.
Notes: TRAINER EXPLANATION: A Permit to Work is a formal, written safety process. It is used for non-routine work that carries significant risk. Think of it as a written conversation between two people: the Permit Issuer, who owns the workplace and knows the plant, and the Permit Receiver, who will do the work. The permit makes everyone pause – a 'Time Out for Safety' – before any tool is lifted or valve is turned. SIMPLE EXAMPLE: Maintenance wants to replace a mechanical seal on a process pump. Operations owns that pump and knows what gas is in it and what is connected to it. The permit is how Operations and Maintenance agree, in writing, how the job will be made safe. ASK THE TRAINEES: Why do you think the permit needs two people – an Issuer and a Receiver – and not just one? EXPECTED ANSWER: Because the Issuer knows the plant and its hazards, and the Receiver knows the job. Together they cover what one person alone could miss. TRAINER REMINDER: The permit protects people, assets, the environment and operational integrity. It is a safety process, not just a form. ANIMATION: Click to show Issuer, then the permit link, then Receiver, then the purpose bar. SOURCE: Module 7 Course Notes – Section 1.1.1

## Slide 6: 7 Questions Every Permit Must Answer
Before any tool is lifted or any valve is turned, the PTW answers:
WHAT & WHERE?
Exactly what work, and exactly where
WHEN?
When will it be done, and for how long?
WHO?
Who will do it – are they competent?
HAZARDS?
What hazards exist for this task, here, now?
CONTROLS?
What controls & isolations are needed – and verified?
EMERGENCY?
What if conditions change or something goes wrong?
RESTORE?
How will the area be made safe and operable again?
Notes: TRAINER EXPLANATION: Every permit must answer seven simple questions. What and where. When and how long. Who – and are they competent. What are the hazards for this task, in this place, at this time. What controls are needed – and have they been checked. What is the emergency plan. And how will we put the area back to a safe state when we finish. If a permit cannot answer all seven, it is not ready. SIMPLE EXAMPLE: For a flange break on a gas line: WHAT – remove a spool piece; WHERE – a specific tagged line; WHO – the named mechanical crew; HAZARDS – trapped pressure, flammable gas, H2S; CONTROLS – isolation, blinds, gas test; EMERGENCY – escape route and alarm; RESTORE – re-bolt, remove blinds, hand back. ASK THE TRAINEES: Which question do you think is most often answered badly? EXPECTED ANSWER: Often 'hazards' and 'controls verified' – people assume instead of checking. The Course Notes say the PTW moves safety from 'passive assumption' to an 'active, verified state'. TRAINER REMINDER: Documented answers make safety ACTIVE and VERIFIED, not assumed. ANIMATION: Each question appears on click. SOURCE: Module 7 Course Notes – Section 1.1.1

## Slide 7
KEY MESSAGE
A permit is NOT just a piece of paper
Walk the worksite
Find the hazards
Agree the controls
Physically verify isolations
Brief the crew face-to-face
Notes: TRAINER EXPLANATION: Here is a dangerous misconception: that the PTW is a tick-box exercise – a piece of paper you sign to get started. The Course Notes reject that view completely. The paper is only the output. The real value is in the activities behind it: walking the site, brainstorming the hazards, debating the controls, physically verifying the isolations and briefing the crew face to face. SIMPLE EXAMPLE: Two permits can look identical on paper. One was signed in the office; the other was signed after the Issuer and Receiver walked to the pump together and checked every lock. Only the second one is a real permit. ASK THE TRAINEES: What could happen if a permit is signed in the office without visiting the site? EXPECTED ANSWER: A wrong valve could be locked, a blind could be missing, or gas could still be present – and nobody would know until the line is opened. TRAINER REMINDER: The PTW is a quality-assurance process for safety: planned controls must be concretely in place and understood by all before the 'go' decision. ANIMATION: Click to reveal the five activities one by one. SOURCE: Module 7 Course Notes – Section 1.2.1

## Slide 8: What Can Go Wrong? Without vs. With PTW
Example: a flange must be opened on a process line that contained flammable gas and H₂S
WITHOUT an effective PTW
No permit / tick-box
Hazards not identified
Isolation not verified
Flange opened
Gas release, fire or exposure
WITH an effective PTW
Plan & JSA
Identify hazards
Isolate & lock
Verify zero energy
Gas test
Authorise & sign
Brief crew
Work, monitor, close
Notes: TRAINER EXPLANATION: Let us look at the same job done two ways. Without an effective PTW, the hazards are not identified, nobody verifies the isolation, the flange is opened and gas comes out. With PTW, we plan, identify the hazards, isolate, prove the line is at zero energy, test the atmosphere, authorise, brief the crew, and then work and monitor until closure. SIMPLE EXAMPLE: The Course Notes describe 'System Integrity Breach' – breaking a flange or opening a vessel – as one of the conditions that brings work into PTW scope. They also use 'Release of Flammable Gas' as the example top event in the bow-tie model. That is exactly the risk on this slide. ASK THE TRAINEES: Looking at the green chain – which single step, if skipped, would most likely lead straight to the red outcome? EXPECTED ANSWER: Verifying the isolation (VOI). The Course Notes call this 'the final critical step before the permit is signed'. TRAINER REMINDER: Do not exaggerate – the point is simply that each PTW step closes a gap that could otherwise lead to release, fire or exposure. ANIMATION: Click 1 shows the 'without' chain; click 2 the 'with' panel; then each green step wipes in. SOURCE: Module 7 Course Notes – Sections 1.1.2, 5.3.3, 6.3.3

## Slide 9: Why We Need PTW – 8 Objectives
Identify hazards
Formal review of the task and the work environment
Assure controls
Controls planned AND physically verified
Clear authorisation
Written roles and accountabilities
Communication
Hazards, controls & emergency info passed on
Coordination
Prevents clashes between work groups
Legal compliance
Verifiable audit trail of due diligence
Permanent record
What, where, when, by whom, under what controls
Safety culture
Planning over rushing; anyone may question safety
Notes: TRAINER EXPLANATION: The Course Notes list eight objectives that together form a safety net. The first two are the heart of it: identify the hazards, and make sure the controls are not just planned but physically verified. Then: clear written authorisation, good communication between teams and shifts, coordination so two jobs do not clash, legal compliance, a permanent record, and a culture where planning beats rushing. SIMPLE EXAMPLE: Coordination: the PTW log in the control room shows all active permits. If one crew plans hot work next to another crew breaking a flange on a gas line, the log helps spot the conflict before either job starts. ASK THE TRAINEES: Why would a permanent record of permits be useful? EXPECTED ANSWER: For incident investigation, audits, management review and learning – the record shows what was done, where, when, by whom and under what controls. TRAINER REMINDER: Toolbox talks based on the permit are part of the communication objective – they are mandatory, not optional. ANIMATION: Top row on click 1, bottom row on click 2. SOURCE: Module 7 Course Notes – Section 1.1.3

## Slide 10: PTW is a Legal Duty, Not a Choice
Duty of care
PTW is part of the legal duty to take all reasonable steps to keep workers, contractors and the public safe.
Examples named in the Course Notes
ISO 45001 · ILO C155 & C187 · OSHA PSM 1910.119 · OSHA LOTO 1910.147 · Confined spaces 1910.146 · UK HSWA 1974 & COMAH 2015 · Energy Institute PTW Guidance · API · IOGP Life-Saving Rules
If PTW fails, the consequences include:
Large fines for the organisation
Criminal prosecution of managers & supervisors
Insurance claims invalidated
Reputation damage & loss of licence to operate
Notes: TRAINER EXPLANATION: PTW is not just company policy. It is part of an organisation's legal 'duty of care' – the obligation to take all reasonable steps to keep people safe. International standards, national laws and industry guidance all expect a formal work-control system for high-risk work. After an incident, inspectors and courts look at the permit documents. Missing or poor permits can be used as evidence of negligence. SIMPLE EXAMPLE: If an incident happens during a vessel entry, the first thing investigators ask for is the permit, the gas test certificate and the isolation certificate. ASK THE TRAINEES: After an incident, what is the first document an investigator will ask for? EXPECTED ANSWER: The permit and its attached certificates. TRAINER REMINDER: Trainees do not need to memorise the list of standards – the key point is that PTW is a legal expectation and poor permits have serious consequences. Your site procedure is the document you follow. SOURCE: Module 7 Course Notes – Section 1.2.2

## Slide 11
SECTION 2
When is PTW Required? Principles & the Life Saving Rule
The scope, the seven principles and the one rule we never break
Notes: TRAINER EXPLANATION: Now we look at WHEN a permit is needed, the principles that make PTW work, and the Life Saving Rule. SOURCE: Module 7 Course Notes – Sections 1.1.2, 1.3, 1.4

## Slide 12: When is a Permit Required?
NON-ROUTINE WORK + SIGNIFICANT RISK = PTW required
Fire or explosion
Ignition sources where flammable atmospheres may exist
Toxic / asphyxiating atmosphere
Hazardous gases, vapours or low oxygen
Stored energy
Electrical, mechanical, hydraulic, pneumatic, chemical, thermal…
Entrapment / engulfment
Collapse, engulfment or entrapment possible
Height or depth
A fall from height or into depth
Breaking containment
Breaking into a process system, pipeline or vessel
Notes: TRAINER EXPLANATION: A permit is required for NON-ROUTINE work that carries SIGNIFICANT RISK. Non-routine means it is not part of normal operating procedures – usually maintenance, construction, inspection or repair. Significant risk is decided by risk assessment, and typically means one or more of these six conditions: fire or explosion, toxic or low-oxygen atmosphere, stored energy, entrapment or engulfment, height or depth, or breaking into a process system. SIMPLE EXAMPLE: An operator doing a routine plant round under the normal operating procedure does not need a permit. But opening a flange on a process line is 'breaking containment' – that is in PTW scope. ASK THE TRAINEES: Is replacing a valve on a process gas line routine or non-routine? Which box does it fall into? EXPECTED ANSWER: Non-routine. It is 'breaking containment' and may also involve stored energy (pressure) and toxic/flammable gas. TRAINER REMINDER: The scope is defined in the site Safety Management System, and bypassing PTW for an in-scope activity is a disciplinary offence. ANIMATION: Each hazard card appears on click. SOURCE: Module 7 Course Notes – Section 1.1.2

## Slide 13: The 7 Principles of an Effective PTW System
Competency
Everyone trained, assessed and authorised for their role
Clarity
Exact work, location, hazards, controls and validity
Positive control & verification
Controls physically checked before authorisation
Communication
Handover, briefing, permit displayed at site
Consistency
Same forms, terms and procedures across the site
Strict compliance
Permit conditions are instructions, not suggestions
Continuous monitoring
Issuer checks the site; Receiver supervises the work
Notes: TRAINER EXPLANATION: For PTW to be more than a paper exercise, it stands on seven principles. Competency is the foundation – every person in the chain must be trained and authorised. Clarity – the permit must be precise. Positive control – the Issuer only authorises after personally verifying, often by walking the site. Communication – handovers, briefings and displaying the permit. Consistency – the same forms everywhere. Strict compliance – no deviations unless the permit is formally suspended and re-authorised. And continuous monitoring during the work. SIMPLE EXAMPLE: Positive control is like an electrical circuit: the permit is the switch that lets work start, but the verification is what closes the safety circuit. ASK THE TRAINEES: Which principle is described as 'the foundation'? EXPECTED ANSWER: Competency. TRAINER REMINDER: Deviations from a permit are forbidden unless it is formally suspended, revised and re-authorised. SOURCE: Module 7 Course Notes – Section 1.3.1

## Slide 14: Clarity: Vague Permits Cause Incidents
VAGUE – DON’T
“Work on the pump”
“Area around the tank”
“Isolate pump”
No times, or AM/PM confusion
CLEAR – DO
“Replace mechanical seal on Pump P-101A. Pump Alley 1, Cell 3, at Grade.”
“NO work is authorised on the motor or coupling.”
“Close and lock XV-101A & XV-101B, install blind at Flange F-101.”
Valid 08:00 – 16:30 (24-hour format)
Ambiguity is a direct pathway to error and incident.
Notes: TRAINER EXPLANATION: Clarity is one of the most practical principles. A vague permit lets people drift onto the wrong equipment or do tasks nobody assessed. A clear permit names the exact equipment, location, controls and times. It also says what is NOT authorised – the Course Notes call that phrase 'powerful and necessary'. SIMPLE EXAMPLE: In a gas plant you may have Pump P-101A and its standby P-101B side by side. 'Work on the pump' could mean either. Only one is isolated. A clear permit removes that risk. ASK THE TRAINEES: Why should permit times be written in 24-hour format? EXPECTED ANSWER: To avoid AM/PM confusion. TRAINER REMINDER: Every example on the right is taken from the Course Notes. Precise descriptions prevent 'scope creep'. ANIMATION: Click 1 vague, click 2 clear, click 3 key line. SOURCE: Module 7 Course Notes – Sections 1.3.1, 6.2.2, 8.1.2

## Slide 15: Layers of Protection (Defence-in-Depth)
Layer 1 Elimination / Substitution
Layer 2 Engineering controls
Layer 3 Procedural control – PTW
Layer 4 Supervision & monitoring
Layer 5 PPE
If one layer fails…
…the next should catch it. A flawed risk assessment should be caught by the Issuer’s verification.
Swiss-cheese model
Roles overlap. If an Issuer misses a hazard, the Receiver or Safety Officer is there to catch it.
Notes: TRAINER EXPLANATION: PTW is one layer in a set of defences. First we ask: can we eliminate the hazard? Then engineering controls like alarms and relief valves. Then the PTW procedure itself. Then supervision during the work. And last, PPE. The idea is simple: if one layer fails, the next layer catches it. Our roles work the same way – like slices of Swiss cheese, the holes in one slice are covered by the next. SIMPLE EXAMPLE: If the JSA for a pump job forgets that the bypass line from the standby pump is still live, the Permit Issuer – who knows the plant – should catch it during review. ASK THE TRAINEES: Why is PPE the LAST layer and not the first? EXPECTED ANSWER: Because PPE does not remove the hazard; it only protects the worker if it is the right type, worn correctly and does not fail. TRAINER REMINDER: The PTW process should ask the elimination question first: can this hazardous work be avoided? SOURCE: Module 7 Course Notes – Sections 1.3.2 and 3.8 Conclusion

## Slide 16
LIFE SAVING RULE · WORK AUTHORISATION
“Work must not be performed without a valid permit where a permit is required.”
No “quick job” exceptions
Verbal approval is NOT valid
Applies to employees, contractors, visitors
Violation = gross misconduct
Notes: TRAINER EXPLANATION: This is the Life Saving Rule for work authorisation: work must not be performed without a valid permit where a permit is required. Life Saving Rules are few, simple, and cover activities where breaking the rule is likely to lead to death or life-changing injury. There is no such thing as a 'quick job' that justifies skipping the permit. Verbal or implied approval is not valid – the authorisation exists only in the signed, written permit. The rule applies to everyone. Breaking it is gross misconduct and usually means immediate removal from site. SIMPLE EXAMPLE: A supervisor says: 'It's just ten minutes with a grinder on that support – go ahead, I'll sort the paperwork later.' That is a verbal authorisation for hot work. It is not valid and breaks the Life Saving Rule. ASK THE TRAINEES: Who does this rule apply to? EXPECTED ANSWER: Everyone – company employees, contractors, subcontractors and visitors. One standard. TRAINER REMINDER: This rule is the bedrock of the whole PTW system. Enforcement happens within a 'just culture' that also encourages reporting near misses without fear of blame. SOURCE: Module 7 Course Notes – Sections 1.4.1 and 1.4.2

## Slide 17: Is the Permit VALID? 5 Checks
A permit is valid only when ALL five are true at the same time:
Fully completed
Every required field filled in – nothing missing
Original signatures
Handwritten Issuer & Receiver signatures – not copied or stamped
Within validity
Inside its date & time – an expired permit is void
Certificates attached & current
Gas test, isolation etc. – within re-test intervals
Site matches the permit
Any change invalidates it until re-assessed
Valid permit = all 5 checks
Notes: TRAINER EXPLANATION: How do you know a permit is valid? Five things must all be true at the same moment. It is fully completed. It has the original handwritten signatures of the Issuer and Receiver. It is within its date and time. All the attached certificates – such as the gas test and the isolation certificate – are there and still current. And the actual worksite matches what the permit says. If any one of these is missing, the permit is not valid. SIMPLE EXAMPLE: A vessel-entry permit is signed and in date, but the gas test was done four hours ago and the re-test interval has passed. The permit is no longer valid until the atmosphere is re-tested. ASK THE TRAINEES: If the wind changes direction during outdoor hot work, is the permit still valid? EXPECTED ANSWER: Not automatically – conditions have changed. Any change invalidates the permit until it is re-assessed; hot work revalidation is required if conditions change, for example wind direction. TRAINER REMINDER: The signed permit (or a verified copy) must be posted at the worksite for the whole job – for the crew, auditors and emergency responders. SOURCE: Module 7 Course Notes – Sections 1.4.2 and 2.1.4

## Slide 18: Trainer Question: “It’s only a quick job…”
A small leak needs a quick fix. The supervisor says: “No time for a permit – I give you verbal OK.”
Can the technician start the work?
THINK FIRST… then click to reveal the answer
NO. Verbal or implied authorisation is invalid. Authorisation exists only in the signed, written permit.
Why? There is no “quick job” exception – the Life Saving Rule applies to everyone.
Do: Use your Stop Work Authority, raise a permit request and wait for a valid, signed permit.
Notes: TRAINER EXPLANATION: Read the situation aloud and let the group answer before you click. This is the most common pressure point in real life – a small job, time pressure, and a supervisor offering a verbal OK. SIMPLE EXAMPLE: The Course Notes include a real-style example: a worker was found grinding without a Hot Work Permit because the supervisor told him to start under time pressure. The root cause was that small reactive jobs were not being planned. ASK THE TRAINEES: How would you say 'no' politely but firmly to your supervisor? EXPECTED ANSWER: For example: 'I can't start without a valid permit – it's a Life Saving Rule. Let's raise the permit now.' Every person has the right and the duty to stop unsafe work. TRAINER REMINDER: Stop Work Authority is protected by policy. No production goal is more important than this rule. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 1.4.2, 7.4, 11.3.3

## Slide 19
SECTION 3
Types of Work Permits
Which permit for which job – and the key controls for each
Notes: TRAINER EXPLANATION: Different jobs have different hazards, so we use specialised permits. Remember: permit types often combine – one job can need several. SOURCE: Module 7 Course Notes – Section 2.0

## Slide 20: The Permit Family at a Glance
Hot Work
Heat, sparks or flame
Cold Work
No ignition source, but significant risk
Confined Space Entry
Entry into vessels, tanks, pits
Electrical Work
Work on or near electrical systems
Excavation
Any digging, trenching, boring
Work at Height
Where a fall could cause injury
Radiography
Industrial X-ray / gamma sources
Specialised
SIMOPS, Break of Containment, MOC…
Notes: TRAINER EXPLANATION: Here is the whole permit family. Seven main types – hot work, cold work, confined space entry, electrical, excavation, work at height and radiography – plus combined and specialised permits. Each permit tailors the general PTW principles to a specific hazard. These are not separate boxes: they frequently overlap. SIMPLE EXAMPLE: The Course Notes give this example: repairing a pump motor inside a vessel using welding would need an Electrical Work Permit, a Confined Space Entry Permit and a Hot Work Permit – all integrated together. ASK THE TRAINEES: Can one job need more than one permit type? EXPECTED ANSWER: Yes. Permits frequently overlap and must be combined, not issued in isolation. TRAINER REMINDER: Use the next slides to go into each type; keep this slide as the 'map'. SOURCE: Module 7 Course Notes – Section 2.0 Introduction and 1.1.2

## Slide 21: Hot Work Permit
Heat · Sparks · Flame
Typical activities
Welding, cutting, brazing
Grinding, abrasive cutting, blasting
Open-flame torches / heating
Non-intrinsically-safe electrical tools
Drilling or chipping that makes heat or sparks
Hazards
Primary: ignition of flammable gas, vapour, liquid or solids
Secondary: fire spread, explosion, toxic fumes, burns, welder’s flash, shock
Hidden: pyrophoric (self-igniting) materials, hidden pockets of flammables
Notes: TRAINER EXPLANATION: A Hot Work Permit is needed for any job that produces enough heat, sparks or flame to ignite flammable or combustible materials. The Course Notes call it the most common and potentially most dangerous permit, because it brings an ignition source into an area that may contain flammable gas. Note that it is not only welding: grinding, open flames and even ordinary non-intrinsically-safe power tools and extension cords count. SIMPLE EXAMPLE: In a gas treatment plant, grinding a corroded pipe support next to a live process area is hot work. Even a standard electric drill can be an ignition source. ASK THE TRAINEES: Is using a normal (non-certified) power drill in a process area hot work? EXPECTED ANSWER: Yes – non-intrinsically safe electrical equipment is listed as in-scope for hot work. TRAINER REMINDER: Watch for hidden hazards – pyrophoric scale and hidden pockets of flammables inside ducts or double-walled structures. SOURCE: Module 7 Course Notes – Section 2.1.1–2.1.2

## Slide 22: Hot Work – Key Controls
≤ 10%
LEL alarm setting – STOP if readings exceed 10% LEL
19.5 – 23.5%
Oxygen range in confined / poorly ventilated areas
15 m
Clear combustibles (or cover with flame-retardant blankets)
+ 60 min
Fire watch stays at least 60 minutes after hot work ends
Gas monitoring
Continuous combustible-gas monitoring before and during hot work. Calibrated & bump-tested daily. Placed where gas may collect (heavier gases settle low).
Fire watch & fire readiness
Dedicated fire watch – no other duties. Trained, with a charged extinguisher (min. 9 kg dry chemical) and communication. Water supply for larger work.
Validity & prohibitions
Valid one shift only (max 12 h). Revalidate after breaks or changes (e.g. wind). FORBIDDEN during hazardous transfers, active hydrocarbon releases or unsafe gas tests.
Notes: TRAINER EXPLANATION: These are the hot-work controls from the Course Notes. Gas monitoring is the non-negotiable first step: continuous combustible-gas monitoring, alarm set at or below 10% LEL, and work stops immediately if the reading goes above 10% LEL. Clear combustibles for at least 15 metres or cover them. A dedicated fire watch with no other duties stays during the work and for at least 60 minutes afterwards. Hot work permits are valid for one shift, maximum 12 hours. SIMPLE EXAMPLE: Welding near operating gas equipment: the gas monitor is placed at the low point near the work because heavier-than-air gases settle there; the fire watch stands by with a 9 kg extinguisher and a radio; drains and openings within 15 m are covered so sparks cannot travel. ASK THE TRAINEES: Why does the fire watch stay for 60 minutes after welding stops? EXPECTED ANSWER: Because smouldering fires can start after the work ends – the fire watch keeps watching the area, including adjacent spaces. TRAINER REMINDER: LEL means Lower Explosive Limit – the lowest concentration of gas in air that can ignite. 10% LEL is only one tenth of that, giving a safety margin. Hot work is absolutely forbidden in areas with active hydrocarbon releases. SOURCE: Module 7 Course Notes – Sections 2.1.3–2.1.4, 3.8.2, 6.6.2

## Slide 23: Cold Work Permit – “Cold” Does Not Mean Low Risk
Typical activities
Pump overhaul, valve replacement
Breaking into process piping (non-live)
Hand tools / non-sparking tools
NDT (not radiography)
Cleaning or degassing
Any task needing LOTO but no hot work
Hazards
Release of hazardous energy (mechanical, hydraulic, pneumatic, chemical)
Toxic / flammable release when breaking systems
Struck-by and caught-between
Key risk: COMPLACENCY
Key controls
Formal isolation plan (LOTO) – the cornerstone
Double block & bleed or positive isolation (blinds) for process systems
Every worker applies a personal lock
Verify zero energy (VOI) before work
Gas test if breaking into systems
Barricades, rigging plans, PPE
Notes: TRAINER EXPLANATION: A Cold Work Permit covers high-risk work that has no ignition source. It is the general-purpose permit for mechanical tasks. The big warning in the Course Notes is complacency: because it is 'cold', people underestimate pressure, chemicals and moving parts. Energy isolation – Lock-Out Tag-Out – is the cornerstone of cold work. SIMPLE EXAMPLE: Replacing a valve on a process line that previously carried sour gas is cold work. There is no flame, but trapped pressure or residual H2S could be released when the line is opened. That is why isolation, verification and possibly gas testing are required. ASK THE TRAINEES: What is the cornerstone control of a Cold Work Permit? EXPECTED ANSWER: Energy isolation (LOTO) with a documented isolation plan and verification of isolation. TRAINER REMINDER: Atmospheric testing may be required even for cold work if the task breaks into systems that could have contained toxics or asphyxiants. SOURCE: Module 7 Course Notes – Section 2.2

## Slide 24: Confined Space Entry – What is a Confined Space?
A confined space has ALL THREE features:
Not designed for continuous occupancy
e.g. vessel, tank, column, pit, duct
Limited entry / exit
Small manway, climbing or crawling needed
Potential hazardous atmosphere or condition
Low/high O₂, flammable gas, toxics (H₂S, CO), engulfment
The entry team
Entrant · Attendant (never enters) · Entry Supervisor · Rescue Team
Confined space entry
Notes: TRAINER EXPLANATION: A confined space must have all three features: it is not designed for people to stay in, it has limited ways in and out, and it may contain a hazardous atmosphere or condition – low or high oxygen, flammable gas, toxic gas like H2S or carbon monoxide, engulfment, moving parts or awkward shapes. Any entry into such a space needs a Confined Space Entry Permit. SIMPLE EXAMPLE: In a gas treatment plant, entering a process vessel or column through a manway for inspection is confined space entry. Even after draining and purging, residual H2S or low oxygen can be present. ASK THE TRAINEES: Who are the four members of the confined space team? EXPECTED ANSWER: The Authorised Entrant, the Attendant (standby person – never enters), the Entry Supervisor (authorises entry and signs), and the pre-designated Rescue Team. TRAINER REMINDER: The Attendant NEVER enters the space under any circumstances. Do not rely on municipal fire services as primary rescue unless pre-arranged and trained on your equipment. SOURCE: Module 7 Course Notes – Sections 2.3.1–2.3.2

## Slide 25: Confined Space Entry – Before & During Entry
1 Isolate
Lock out ALL energy; blind or disconnect all piping
2 Clean & purge
Remove residues; purge with inert gas or air
3 Ventilate
Continuous forced ventilation – natural is NOT enough
4 Gas test
O₂ → Flammables → Toxics; top, middle, bottom
5 Rescue ready
Tripod, winch, harness; rescue team on alert
6 Enter & monitor
Attendant monitors at entrance; constant contact
O₂ 19.5 – 23.5%
Oxygen
LEL < 10%
Flammables
H₂S < 10 ppm
Example toxic limit
1 entry / 4 h
Typical max. validity
Notes: TRAINER EXPLANATION: Here is the confined-space sequence from the Course Notes. Isolate every energy source and blind or disconnect every pipe. Clean and purge. Ventilate continuously with forced air – natural ventilation is not enough. Test the atmosphere in the correct order – oxygen first, then flammables, then toxics – at the top, middle and bottom because gases layer. Have the rescue equipment set up before entry. Then the Attendant monitors continuously at the entrance. SIMPLE EXAMPLE: Before entering a vessel in our plant, the tester lowers the sampling hose and reads oxygen first, then LEL, then H2S, at three levels. The permit states the acceptable entry levels, for example O2 19.5–23.5%, LEL below 10%, H2S below 10 ppm. ASK THE TRAINEES: Why do we test oxygen FIRST? EXPECTED ANSWER: The Course Notes require the order oxygen, flammables, toxics. (Trainer: keep to that order as stated – oxygen level also affects whether the other readings can be trusted.) TRAINER REMINDER: The permit is typically valid for one entry or a maximum of 4 hours. Re-test if the space is vacated and re-entered, or if conditions change. ANIMATION: Steps wipe in one by one; then the four numbers. SOURCE: Module 7 Course Notes – Section 2.3.3 and 6.4.2

## Slide 26: Electrical Work Permit
De-energise first
LV ≤ 1000 V AC
or ≤ 1500 V DC
HV > 1000 V AC
Extra procedures & HV-authorised person
De-energised (preferred)
Identify the right circuit
Isolate, lock & tag
Prove dead: live-dead-live test
Discharge stored energy
Barricade / control access
Energised (last resort)
Only if de-energising is more hazardous or infeasible
Justification & senior approval
Specially trained workers
Arc-flash rated PPE, insulated tools
Detailed shock & arc-flash briefing
Notes: TRAINER EXPLANATION: The Electrical Work Permit covers work on or near electrical systems and works hand-in-hand with LOTO. The rule is a hierarchy: de-energise first – that is always the goal. Working live is a last resort, allowed only if de-energising creates a greater hazard or is not feasible, and it needs extra justification, management approval, trained people, arc-flash PPE and insulated tools. SIMPLE EXAMPLE: Before maintenance on an electric motor driving a process pump, the electrician isolates the breaker, applies a personal lock and tag, and proves the circuit dead with a tester that is checked on a known live source before and after – the 'live-dead-live' test. ASK THE TRAINEES: What does 'live-dead-live' mean? EXPECTED ANSWER: Check the tester on a known live source, test the circuit (dead), then check the tester again on the live source – proving the tester worked. TRAINER REMINDER: Emergency contingency: if someone is electrocuted, DO NOT TOUCH THE VICTIM – de-energise first, or use a non-conductive rescue hook. SOURCE: Module 7 Course Notes – Sections 2.4 and 9.2.2

## Slide 27: Excavation Permit
Find services before you dig
Before digging
Notify utility owners 24–48 h ahead. Use up-to-date drawings – but never rely on drawings alone. Locate ALL services (cable/pipe locators, potholing) plus 1–2 m buffer.
Around the trench
Spoil at least 0.6 m from the edge. Ladder or ramp within 7.5 m in trenches > 1.2 m. Test atmosphere before entry. Inspect daily and after rain or vibration.
Protection by depth
< 1.2 m
Basic precautions if competent ground verified
1.2 – 4.5 m
Protective system: sloping/benching, shoring or trench box
> 4.5 m
Design approved by a Professional Engineer
Notes: TRAINER EXPLANATION: An Excavation Permit is needed for any digging, trenching or boring. The two big risks are hitting underground services and collapse. So we notify utility owners 24 to 48 hours in advance, use drawings but never rely on them alone, and physically locate every service. The deeper the excavation, the stronger the protection: basic precautions under 1.2 m if the ground is verified competent, a protective system between 1.2 and 4.5 m, and an engineer-approved design beyond 4.5 m. SIMPLE EXAMPLE: Digging a trench in a gas plant to lay a new cable may cross buried process lines or live cables. Locating them with a cable locator or by careful potholing before machine digging prevents a strike. ASK THE TRAINEES: Why do we keep the spoil pile back from the edge? EXPECTED ANSWER: Spoil near the edge adds weight and can make the trench wall collapse or fall onto workers; the Course Notes require at least 0.6 m. TRAINER REMINDER: Contingency: if the trench shows cracking, sloughing or water seepage – evacuate immediately; no re-entry until a competent person inspects. SOURCE: Module 7 Course Notes – Sections 2.5 and 9.2.2

## Slide 28: Work at Height Permit
Prevent the fall
Any work where a person could fall a distance liable to cause injury – can be 2 m or less. Focus: PREVENT the fall.
Fall protection hierarchy
Eliminate – work from the ground
Passive – guardrails, scaffold with toe-boards
Collective – safety nets, airbags
Personal – restraint preferred over arrest
Ladders – short, light work only (3 points of contact)
Scaffold tags
GREEN Safe for use
YELLOW Use with caution
RED Do NOT use
Anchor ≥ 22 kN, free fall ≤ 1.8 m
Full body harness, dorsal D-ring
Rescue plan BEFORE work starts
Notes: TRAINER EXPLANATION: Work at height means any work where a fall could cause injury – sometimes at 2 metres or even less if there are hazards below. The permit focuses on preventing the fall, not just catching it. Follow the hierarchy: eliminate first, then guardrails and scaffolds, then nets, then personal fall protection – and restraint, which stops you reaching the edge, is better than arrest, which stops you after you fall. SIMPLE EXAMPLE: Inspecting a valve on an upper platform of a process column: use a proper scaffold with guardrails and a green tag rather than a ladder. If a harness is used for fall arrest, the rescue plan must be ready before work begins. ASK THE TRAINEES: What does a RED scaffold tag mean? EXPECTED ANSWER: Do not use. TRAINER REMINDER: Scaffolds are built, altered and dismantled only by certified scaffolders; users check daily and a competent person inspects weekly. A fallen worker must be rescued within minutes to avoid suspension trauma. SOURCE: Module 7 Course Notes – Sections 2.6 and 9.4.2

## Slide 29: Radiography Permit (Ionising Radiation)
Invisible hazard
ALARA = As Low As Reasonably Achievable. Every action must minimise radiation exposure.
Dosimeters: Everyone in controlled areas wears active and passive dosimeters
Controlled area: Exclusion zone: tape, signs, flashing lights – no entry during exposure
Supervised area & barriers: Surrounding zone monitored; lead screens / shielded enclosures
Positive communication: Voice, radio and visual signals (e.g. horn before exposure)
Source security: Strict handling, transport and storage – prevent loss or theft
Notes: TRAINER EXPLANATION: Radiography uses X-ray machines or gamma sources to check welds without cutting them. The hazard – ionising radiation – is invisible and potentially lethal. The guiding principle is ALARA: keep exposure as low as reasonably achievable. The work area is divided into a controlled area, where nobody unauthorised may enter during exposure, and a supervised area around it. A radiography safety watch keeps the perimeter clear and monitors with a survey meter. SIMPLE EXAMPLE: When new pipeline welds in the plant are radiographed, barriers and warning lights go up, a horn sounds before exposure, and the Radiation Safety Officer surveys the boundary. ASK THE TRAINEES: You see radiation barrier tape and a flashing light across your normal route. What do you do? EXPECTED ANSWER: Do not cross. Wait or take another route – unauthorised entry into the controlled area is strictly prohibited during exposure. TRAINER REMINDER: Radiography is often night or off-shift work – everyone must respect barriers even when nobody seems to be around. SOURCE: Module 7 Course Notes – Sections 2.7 and 3.8.2 C

## Slide 30: Combined Permits – The Golden Rule
Example from the Course Notes: Vessel entry for catalyst replacement in R-201
MASTER PERMIT
Cold Work Permit – “Catalyst Replacement in R-201”
Confined Space Entry Certificate
Hot Work Certificate (if cutting/welding)
Isolation Certificate (LOTO, blinds)
Scaffold Certificate (internal scaffold)
GOLDEN RULE: The MOST RESTRICTIVE condition on ANY attached permit or certificate governs the whole job. All conditions must be met at the same time.
Notes: TRAINER EXPLANATION: Complex jobs need several hazard controls at once. We do not issue separate permits in isolation – we combine them. A master permit, often the Cold Work Permit, acts as the umbrella, and supplementary certificates are attached for confined space, hot work, isolation and scaffolding. The golden rule: the most restrictive condition on any attached document governs the whole job. SIMPLE EXAMPLE: If the Confined Space Certificate requires continuous ventilation and the Hot Work Certificate requires a fire watch, both must be in place at the same time for work to continue. If ventilation stops, the work stops – even though the fire watch is still there. ASK THE TRAINEES: During this vessel job, ventilation fails but the welder says the fire watch is present, so they can continue. Correct? EXPECTED ANSWER: No. Every condition of every attached certificate must be met simultaneously. Stop work. TRAINER REMINDER: The Permit Issuer's final responsibility is to make sure the complete, integrated safety envelope is established and verified before authorising. SOURCE: Module 7 Course Notes – Section 2.8.1 and 2.8.3

## Slide 31: Specialised Permits
SIMOPS
Two or more potentially conflicting activities close together – coordination meetings, clear boundaries, dedicated SIMOPS coordinator
Break of Containment
The first break into any process system – often supervision present, leak detection, detailed sequence
Management of Change (MOC)
Work that implements an MOC – permit references the MOC number; all MOC safety actions complete
High-Pressure / High-Temperature
Systems outside normal ranges – specialised procedures and materials
Laboratory Work
High-risk chemical synthesis or testing outside standard procedures
Critical Lifting
Complex or heavy lifts where load, method or environment present unusual risk
Notes: TRAINER EXPLANATION: Beyond the main seven, the Course Notes describe specialised permits. Two matter most in a running gas plant. SIMOPS – simultaneous operations – is used when two potentially conflicting high-risk activities happen close together, like a crane lift over live process piping. Break of Containment is the specific, highly controlled permit for the first break into any process system. MOC permits link physical changes to the approved change. High-pressure/high-temperature, laboratory and critical lifting permits cover their own special risks. SIMPLE EXAMPLE: A crane lift of a new heat-exchanger bundle over live gas piping while the unit is running is a SIMOPS situation: the lift and the live process must be coordinated, with clear boundaries and a SIMOPS coordinator. ASK THE TRAINEES: What is a 'Break of Containment' permit for? EXPECTED ANSWER: The first break into any process system containing hazardous chemicals, gases or fluids under pressure or vacuum. TRAINER REMINDER: Which specialised permits exist on your site is defined by the site procedure – these are the categories described in the Course Notes. SOURCE: Module 7 Course Notes – Sections 1.1.2 and 2.8.2

## Slide 32: Trainer Question: Which Permit?
Match each job to the permit(s) needed, based on the Course Notes.
Which permit applies?
THINK FIRST… then click to reveal the answer
Grinding a pipe support near a process unit → Hot Work Permit (+ continuous gas monitoring, fire watch)
Replacing a valve on an isolated process line → Cold Work Permit with isolation (LOTO) – gas test if breaking into the system
Welding inside a vessel → Master permit + Confined Space + Hot Work + Isolation certificates
Digging a trench for a new cable → Excavation Permit (locate all services first)
Notes: TRAINER EXPLANATION: Read each job and ask the group to name the permit before you click. Encourage them to name every permit when jobs combine. SIMPLE EXAMPLE: The vessel-welding job is the classic combined permit: the Course Notes' catalyst-replacement example uses a Cold Work master permit with Confined Space, Hot Work, Isolation and Scaffold certificates. ASK THE TRAINEES: For the vessel welding: which condition wins if two certificates say different things? EXPECTED ANSWER: The most restrictive condition governs. TRAINER REMINDER: Final decisions on permit type are made by the Permit Issuer using the site procedure. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 2.1–2.5, 2.8

## Slide 33
SECTION 4
Roles & Responsibilities
Who does what – and what each role must NOT do
Notes: TRAINER EXPLANATION: PTW is a human system. It only works if every person understands their own duties, the limits of their authority and how they depend on others. SOURCE: Module 7 Course Notes – Section 3.0

## Slide 34: The PTW Team – Who is Who?
Project / Operations Manager
Owns the system & culture; provides resources
Permit Coordinator
Runs the permit log; screens requests; spots clashes
Permit Issuer
Owns workplace safety; verifies & authorises
Permit Receiver
Owns safe execution; briefs & supervises crew
Area Authority
Local “eyes & ears”; performs isolations as directed
Isolating Authority
Plans, performs & verifies isolations; signs Isolation Cert.
Safety Officer (HSE)
Independent advice & audits; can recommend suspension
Work Team & Attendants
Follow the permit; Fire Watch, CS Attendant, Radiography Watch
Notes: TRAINER EXPLANATION: Here are the eight roles in the Course Notes. The two most important for daily work are the Permit Issuer – who owns the safety of the workplace and authorises the work – and the Permit Receiver – who owns the safe execution of the work. Around them: the Coordinator manages the permit log; the Area Authority and Isolating Authority handle local knowledge and isolations; the Safety Officer gives independent advice and audits; and the work team and attendants carry out the job. SIMPLE EXAMPLE: For a pump seal replacement: the Operations Shift Supervisor is the Issuer, the Maintenance Supervisor is the Receiver, the area operator closes the valves, the Isolating Authority verifies zero pressure and signs the Isolation Certificate, and the mechanics do the work. ASK THE TRAINEES: Which role is described as 'the eyes and ears' of operations in a plant area? EXPECTED ANSWER: The Area Authority (Operations Representative). TRAINER REMINDER: Each role is a link in a safety chain. A breakdown in one role weakens the entire system. SOURCE: Module 7 Course Notes – Sections 3.1–3.8

## Slide 35: Permit Issuer vs. Permit Receiver
PERMIT ISSUER
“Guardian of the Workplace” – e.g. Operations Shift Supervisor
Reviews the request, method statement and JSA – challenges assumptions
Specifies isolations & controls (Isolation Plan)
Joint site walkdown – NOT optional
Personally verifies controls, then signs FIRST
Revalidates, monitors, suspends and closes
LIMIT: Cannot authorise work outside their area or on systems they are not competent in
PERMIT RECEIVER
“Guardian of the Work” – e.g. Maintenance Supervisor / Foreman
Independently checks scope, hazards & controls – may challenge the Issuer
Accepts and signs; briefs EVERY team member
Continuous direct supervision of the work
Stops work if conditions change; informs Issuer
Shift handover, site restoration, returns permit
LIMIT: Cannot alter permit conditions or accept a permit they do not fully understand
Notes: TRAINER EXPLANATION: These two roles are the heart of PTW. The Issuer is the guardian of the workplace: they review the request, specify the isolations and controls, walk the site with the Receiver, personally verify the controls and only then sign. The Receiver is the guardian of the work: they independently check the permit, accept it, brief every worker, supervise continuously and stop the work if conditions change. SIMPLE EXAMPLE: At signing, the Issuer says: 'I have verified the area is safe for work to commence.' The Receiver then says: 'I accept responsibility for performing the work within these defined conditions.' The Issuer always signs first. ASK THE TRAINEES: The Receiver is not happy with one of the controls. Should they sign anyway to keep the job on schedule? EXPECTED ANSWER: No. The Receiver has the right and duty to challenge the Issuer and must not accept a permit they do not fully understand or agree with. TRAINER REMINDER: The Issuer needs the 'moral courage to say no'. Any change to permit conditions requires suspension and re-issue by the Issuer. SOURCE: Module 7 Course Notes – Sections 3.3, 3.4, 4.3.2

## Slide 36: Supporting Roles – Duties and Limits
Role | Main duties | Must NOT…
Project / Operations Manager | Owns the PTW system; provides resources; enforces Life Saving Rules; leads by example (VFL) | Cannot authorise a specific permit or order PTW steps to be bypassed
Permit Coordinator | Keeps the master Permit Log; screens applications; flags SIMOPS conflicts; tracks expiry | Administrative only – cannot authorise work or approve controls
Area Authority | Local knowledge; performs isolations as directed; monitors area operations | Does not issue permits; acts on Issuer / Isolating Authority instructions
Isolating Authority | Develops isolation plan; supervises isolation; performs VOI; signs Isolation Certificate | Focuses only on isolation – does not authorise the permit
Safety Officer (HSE) | Custodian of procedure; trains; unannounced audits; technical advice; investigations | Cannot issue permits – advisory role; may recommend suspension
Notes: TRAINER EXPLANATION: This table shows the supporting roles. Notice the third column: every role also has limits. The Manager owns the system but cannot authorise individual permits or order people to bypass steps. The Coordinator is an administrator, not a technical authority. The Area Authority executes isolations but does not issue permits. The Isolating Authority has the final technical say on isolation, but does not authorise the overall permit. The Safety Officer advises and audits but cannot issue permits. SIMPLE EXAMPLE: If the Coordinator sees that a hot work permit and a flange-break permit are requested on the same pipe rack at the same time, they flag the SIMOPS conflict and can hold the processing until the Issuers resolve it. ASK THE TRAINEES: Who has the final technical say on whether an isolation is adequate? EXPECTED ANSWER: The Isolating Authority – their certificate is a mandatory prerequisite for the Permit Issuer. TRAINER REMINDER: Knowing the LIMITS of each role prevents the dangerous assumption that 'someone else' is responsible. SOURCE: Module 7 Course Notes – Sections 3.1, 3.2, 3.5, 3.6, 3.7

## Slide 37: The Work Team & Attendants
Every worker must…
Attend the briefing – and ask if anything is unclear
Understand the permit – hazards, controls, emergency actions
Comply – permit conditions, isolation boundaries, PPE
Stay aware – report changes or unsafe conditions at once
Use Stop Work Authority – without fear of reprisal
Fire Watch
Sole duty: watch for fire. Trained. Charged extinguisher + radio. Stays ≥ 60 min after hot work.
Confined Space Attendant
Counts entrants, constant contact, monitors at entrance, summons rescue. NEVER enters.
Radiography Safety Watch
Keeps people out of the controlled zone; survey meter; contact with radiographer.
Notes: TRAINER EXPLANATION: Every single worker holds the most basic responsibility: their own safety and their colleagues' safety. That means attending the briefing, understanding the permit, following it, staying alert and stopping work if something is wrong. Some jobs also need special attendants: the Fire Watch, the Confined Space Attendant and the Radiography Safety Watch. Each has ONE job – and must not be distracted by other tasks. SIMPLE EXAMPLE: During welding near a process pump, the fire watch is asked to 'quickly fetch a tool'. They must refuse – the fire watch has no other duties. ASK THE TRAINEES: An entrant collapses inside a vessel. What does the Attendant do? EXPECTED ANSWER: Raise the alarm, start non-entry rescue (tripod/winch) if possible and summon the rescue team – but NEVER enter the space and never attempt a solo rescue. TRAINER REMINDER: Stop Work Authority belongs to every worker. Use it without fear. SOURCE: Module 7 Course Notes – Section 3.8, 9.2.2

## Slide 38: Trainer Question: Who Does What?
Quick-fire quiz – answer out loud before each click.
Who is responsible?
THINK FIRST… then click to reveal the answer
Who signs FIRST to authorise the work? The Permit Issuer (after verifying the site)
Who briefs the work crew? The Permit Receiver – toolbox talk using the permit
Who must NEVER enter the confined space? The Confined Space Attendant
Can the Safety Officer issue a permit? No – advisory and assurance role only
Who can STOP unsafe work? EVERYONE on site – any time
Who certifies the isolation? The Isolating Authority (Isolation Certificate)
Notes: TRAINER EXPLANATION: Run this as a fast quiz. Ask each question, let trainees shout the answer, then click to confirm. TRAINER REMINDER: The last answer is the most important: Stop Work Authority belongs to every person on site, including visitors and the newest apprentice. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 3.3–3.8, 7.4

## Slide 39
SECTION 5
The PTW Process – From Request to Closure
Seven stages, each with clear owners and handovers
Notes: TRAINER EXPLANATION: The permit is not a static document – it is a process with a lifecycle. At each stage, information is exchanged, checks are made and responsibility is formally handed over. SOURCE: Module 7 Course Notes – Section 4.0

## Slide 40: The PTW Lifecycle – 7 Stages
1 Apply & plan
Requestor completes application + JSA
2 Review risk
Issuer reviews JSA; isolation plan; controls
3 Issue
Joint walkdown, verify, sign
4 Brief
Receiver’s toolbox talk with crew
5 Work & monitor
Stay inside the permit; watch for change
6 Complete
Finish, clean up; locks stay ON
7 Close / extend / cancel
Final walkdown, sign-off, archive
Notes: TRAINER EXPLANATION: Here is the full lifecycle. One: the requestor applies and plans, with a JSA. Two: the Issuer reviews the hazards and writes the isolation plan and controls. Three: the Issuer and Receiver walk the site, verify and sign. Four: the Receiver briefs the crew. Five: the work is done and monitored. Six: the work is completed and the site cleaned – but locks stay on. Seven: the permit is closed, extended or cancelled. It is a closed loop – every permit becomes data for improving future work. SIMPLE EXAMPLE: A pump seal job: the planner raises the application on Monday, the Issuer reviews it, on Tuesday morning they walk down and sign, the crew is briefed, the seal is changed, the site is cleaned, and the permit is closed after the final walkdown. ASK THE TRAINEES: At which stage does responsibility for the workspace pass from Operations to Maintenance? EXPECTED ANSWER: At Stage 3 – Issue: after the joint walkdown and signatures, custodial responsibility transfers from the Issuer to the Receiver. TRAINER REMINDER: Each stage has an output and a handoff. The workflow is a closed loop. ANIMATION: Stages wipe in one at a time. SOURCE: Module 7 Course Notes – Sections 4.0–4.7

## Slide 41: Stages 1–2: Apply, Plan and Review the Risk
1 · The application must include
Precise work description – “Replace mechanical seal on Pump P-101A”, not “fix the pump”
Exact location – plant, unit, tag numbers (P&ID mark-up)
Planned start / end date & time
People – Receiver name and crew size
Attachments – JSA / TRA, method statement, drawings, MOC number
Permit types expected (e.g. Hot Work, Confined Space)
→ Coordinator checks completeness, logs it, sends to the Issuer
2 · Issuer’s review
Challenge the JSA – are all hazards found? controls enough?
Interface hazards: adjacent operations, live utilities, wind/rain, SIMOPS
Isolation Plan: valves to lock, blinds, DBB, electrical points, VOI method
Specify controls: gas testing, fire prevention, PPE, barriers, emergency plan
→ Output: permit draft + isolation plan = the “safe envelope”
Notes: TRAINER EXPLANATION: Stage one is the application. It must be precise: the exact job, the exact equipment and location, times, people, and the planning documents – especially the JSA. The Coordinator screens it and logs it. Stage two is the Issuer's review. The Issuer uses their plant knowledge to challenge the JSA and add hazards the maintenance team may not see – adjacent operations, live utilities, weather, other jobs nearby. Then they write the Isolation Plan and specify every control. SIMPLE EXAMPLE: From the Course Notes: the JSA says 'isolate pump'. The Issuer turns that into 'Close and lock valves XV-101A and XV-101B, install blind at Flange F-101 per drawing SK-101' – and adds 'note: the bypass line from P-101B remains live'. ASK THE TRAINEES: Why is the Issuer – and not the maintenance team – best placed to spot interface hazards? EXPECTED ANSWER: Because the Issuer knows the live status of the plant and how systems are interconnected. TRAINER REMINDER: Output of Stage 2: a permit draft with all hazards and controls listed, and a detailed isolation plan – the 'safe envelope'. SOURCE: Module 7 Course Notes – Sections 4.1, 4.2, 5.4.2

## Slide 42: Stage 3: Walkdown, Verify and Sign
Walk · Check · Sign
1 Meet on site
Issuer + Receiver at the job with the draft permit
2 Check line by line
Sight every lock, tag & blind; review gas tests; check equipment & area
3 Witness VOI
Positive test – try-start / zero pressure – Receiver watches
4 Sign & post
Issuer signs first, then Receiver; time recorded; permit posted; log = ACTIVE
Issuer: “I have verified the area is safe for work to commence.”
Receiver: “I accept responsibility for performing the work within these conditions.”
Notes: TRAINER EXPLANATION: Stage three is where the plan meets reality. The Issuer and Receiver meet at the actual job location with the draft permit and go through every single control: they physically look at each lock, tag and blind, review the gas test, and check that extinguishers, ventilation and barriers are there. Then the isolation is proved with a positive test – Verification of Isolation, or VOI – with the Receiver as witness. Only when both are satisfied do they sign: Issuer first, then Receiver. SIMPLE EXAMPLE: At a pump job, the Issuer points to each padlock on the suction and discharge valves, checks the blind tag number against the permit, then opens a bleed point to show the pressure gauge reading zero. ASK THE TRAINEES: What does VOI stand for, and give one example. EXPECTED ANSWER: Verification of Isolation – for example a try-start of a motor or confirming zero pressure on a gauge. TRAINER REMINDER: After signing: post the original at the worksite, lodge a copy with the Coordinator (log = ACTIVE) and attach supplementary certificates. ANIMATION: Steps wipe in; then the signature statements. SOURCE: Module 7 Course Notes – Section 4.3

## Slide 43: Stage 4: The Toolbox Talk (Pre-Job Briefing)
Brief every worker
Use the posted permit as the agenda
Ask questions to check understanding
Visual PPE check
Workers sign the permit / attendance sheet
T
TASK
What will we do, step by step?
R
RISKS
What are the specific hazards here?
A
ACTIONS
What protects us? Show isolations, gas monitor, extinguisher
H
HELP
If it goes wrong: escape route, Attendant, how to call for help
C
COMMUNICATION
How do we talk during the work? Stop signals?
Notes: TRAINER EXPLANATION: Immediately after accepting the permit, the Receiver gathers the whole team – including the fire watch or attendant – at the worksite with the permit visible. The Course Notes give a simple structure called TRAHC: Task, Risks, Actions, Help and Communication. Then the Receiver checks understanding with questions, checks everyone's PPE, and the workers sign on. SIMPLE EXAMPLE: The Course Notes suggest questions like: 'What's the LEL alarm level on this monitor?' and 'Show me our primary escape path.' For a vessel job, the Receiver points to the tripod, the ventilation fan, the gas monitor and the escape route. ASK THE TRAINEES: What does the 'H' in TRAHC stand for, and what should it cover? EXPECTED ANSWER: Help – the emergency procedure: what to do if something goes wrong, the escape route, who the Attendant is and how to call for help. TRAINER REMINDER: Never assume knowledge carries over: a new shift's crew gets a full briefing, even if the work is continuous. ANIMATION: TRAHC letters wipe in one by one. SOURCE: Module 7 Course Notes – Sections 4.4, 7.2.2

## Slide 44: Stage 5: Doing the Work Safely
Stay inside the permit
Only the task described, at the location stated
Only the tools and methods assessed
Never remove or bypass a lock, tag, barrier or monitor
If anything changes
Receiver STOPS the work immediately
Notify the Issuer – permit is suspended
Resume only after re-assessment (or new permit)
Who watches during the work?
All workers
Leaks, smells, weather, equipment faults
Permit Receiver
Continuous supervision of work & environment
Attendants
Fire watch / confined space duties
Issuer / Area Operator
Periodic spot checks
Safety Officer
Independent compliance audits
Notes: TRAINER EXPLANATION: During the work, the team does only what the permit says: the described task, at the stated location, with the assessed tools – and never bypasses a control. Monitoring is a team sport: every worker watches for leaks and changes, the Receiver supervises continuously, attendants do their dedicated duties, and the Issuer and Safety Officer make checks. If anything changes, the Receiver must stop the work and notify the Issuer – the permit is then effectively suspended. SIMPLE EXAMPLE: While removing insulation for a valve job, the crew finds an extra pipe they did not expect. That is outside the permit – stop, make safe, tell the Issuer. ASK THE TRAINEES: A colleague wants to quickly tighten a leaking flange on the next pipe, 'since we are here anyway'. Allowed? EXPECTED ANSWER: No. Only the task and location described in the permit are authorised. New work needs its own assessment and authorisation. TRAINER REMINDER: If the change is minor and controls are still valid, the Issuer may re-confirm; if significant, the permit may be cancelled and a new one started. SOURCE: Module 7 Course Notes – Section 4.5

## Slide 45: Plant Example: Pump Seal Replacement Step by Step
All details below are taken from examples in the Course Notes
1. Request
“Replace mechanical seal on Pump P-101A, Pump Alley 1, Cell 3. NO work on motor or coupling.” + JSA
2. Issuer review
Adds: “Bypass line from P-101B remains live.”
3. Isolation plan
Close & lock XV-101A and XV-101B; blind at Flange F-101 (drawing SK-101)
4. Walkdown & VOI
Sight every lock & blind; confirm zero pressure; Issuer then Receiver sign
5. Brief & work
TRAHC toolbox talk; hand / air tools as permitted; continuous supervision
6. Complete & close
Clean up; locks stay on until Issuer’s final walkdown; sign closure
Notes: TRAINER EXPLANATION: Let us put the whole lifecycle together with one job that appears throughout the Course Notes – replacing the mechanical seal on Pump P-101A. Follow the six steps: a precise request with a JSA; the Issuer adds a hazard the team missed – the bypass from the standby pump is still live; a specific isolation plan; walkdown with verification of zero energy; toolbox talk and supervised work; then completion and formal closure. SIMPLE EXAMPLE: In a gas plant, P-101A and P-101B are duty and standby pumps. If only P-101A's valves are closed but the bypass from P-101B is live, product could reach the worksite. That is exactly the kind of interface hazard the Issuer must find. ASK THE TRAINEES: Why do the team's locks stay on after the job is finished? EXPECTED ANSWER: Isolations remain in place until the Issuer's final verification; personal locks are removed only after the Issuer confirms it is safe. TRAINER REMINDER: This example shows the HAZOP-style question the Issuer should ask: 'OTHER THAN isolation, could product still reach the worksite?' ANIMATION: Steps appear one by one. SOURCE: Module 7 Course Notes – Sections 4.1–4.7, 5.1.2 C, 5.4.2, 6.2.2

## Slide 46
KEY MESSAGE
No signature without verification
PLAN
VERIFY on site
SIGN
BRIEF
MONITOR
CLOSE
Notes: TRAINER EXPLANATION: If trainees remember one thing from the process section, it is this: no one signs a permit until the controls have been physically verified on site. Then brief, monitor and close formally. ASK THE TRAINEES: What is the difference between a permit signed in the office and one signed after a walkdown? EXPECTED ANSWER: Only the walkdown permit has verified controls – the office permit is based on assumptions. TRAINER REMINDER: Positive control and verification is one of the seven principles: 'The permit is the switch that allows work to begin; the verification is closing the safety circuit.' SOURCE: Module 7 Course Notes – Sections 1.3.1, 4.3

## Slide 47
SECTION 6
Risk Assessment within PTW
Find the hazards, rate the risk, choose the right controls
Notes: TRAINER EXPLANATION: Risk assessment is the 'engine' of the PTW. The permit form gives structure, but the quality of the risk assessment decides how safe the job really is. SOURCE: Module 7 Course Notes – Section 5.0

## Slide 48: How We Find Hazards – 5 Techniques
JSA / TRA
Break the job into steps. For each: What can go wrong? Consequences? Existing controls? More needed?
The foundation tool
“What-If?”
Team asks “What if the blind gasket fails? What if the wind shifts during hot work?”
Complex / novel tasks, SIMOPS
HAZOP mindset
Guide words (NO, MORE, LESS, REVERSE, OTHER THAN…): could product still reach the worksite?
Issuer’s core skill
Site walkdown
Look for corrosion, leaks, odours, staining, congestion, overhead hazards, weather
MANDATORY reality check
Past data
Previous permits, incident reports, maintenance history
“Last time we found H₂S scale…”
Notes: TRAINER EXPLANATION: The Course Notes describe five ways to find hazards. The JSA, or Task Risk Assessment, is the foundation: break the job into steps and ask what can go wrong at each. 'What-If' brainstorming suits complex or new jobs. The HAZOP mindset is the Issuer's skill: using guide words to ask whether product could still reach the worker despite isolation. The site walkdown is mandatory – it checks the paper against reality. And past data tells us what went wrong before. SIMPLE EXAMPLE: From the Course Notes: 'The last time this exchanger was opened, we found H2S scale; therefore specific toxic gas monitoring is required.' History changed the controls for the next job. ASK THE TRAINEES: Which technique is mandatory for every permit? EXPECTED ANSWER: The joint workplace inspection / walkdown immediately before issue. TRAINER REMINDER: Philosophy: 'systematic scepticism' – challenge assumptions and keep asking 'what if?' SOURCE: Module 7 Course Notes – Section 5.1

## Slide 49: Rating the Risk: Severity × Likelihood
RISK = SEVERITY (how bad?) × LIKELIHOOD (how likely during THIS job?)
Severity
Likelihood
Catastrophic – multiple fatalities
Almost certain – sparks when grinding
Major – single fatality
Likely – minor leak breaking a flange
Moderate – lost time injury
Possible – tool dropped from height
Minor – first aid / medical treatment
Unlikely – failure of a properly installed blind
Negligible – no injury
Rare – exceptional circumstances
Action for the permit
HIGH / EXTREME
Cannot proceed – reduce risk first (may need senior approval)
MEDIUM
Proceed with specified controls, supervision & monitoring
LOW
Proceed with routine controls
Notes: TRAINER EXPLANATION: Once we know the hazards, we rate each one. Risk combines severity – how bad could it be – with likelihood – how likely is it during this particular job. The site risk matrix turns that into a rating. High or extreme: the work cannot proceed until additional controls bring it down to medium or lower. Medium: proceed with specified controls, supervision and monitoring. Low: proceed with routine controls. SIMPLE EXAMPLE: Breaking a flange on a gas line: a minor leak is 'likely'. Before controls, the risk could be high. After isolation, blinding, draining and gas testing, the remaining – residual – risk should fall into medium or low. ASK THE TRAINEES: What is the difference between inherent risk and residual risk? EXPECTED ANSWER: Inherent risk is the risk with no controls; residual risk is what remains after all planned controls are applied. The evaluation must consider the residual risk. TRAINER REMINDER: Use your SITE risk matrix for the actual scoring – this slide only shows the categories described in the Course Notes. SOURCE: Module 7 Course Notes – Section 5.2

## Slide 50: Hierarchy of Controls – Start at the Top
ELIMINATION
Remove the hazard
Work in a workshop; wait for full shutdown & depressurisation; avoid entry (cameras)
SUBSTITUTION
Use something less hazardous
Hydraulic cutter instead of grinder; water-based cleaner; low-voltage tool
ENGINEERING
Separate people from the hazard
Isolation & LOTO, ventilation, barriers – the PRIMARY domain of PTW
ADMINISTRATIVE
Change how people work
The permit itself, procedures, toolbox talks, signage, time limits
PPE
Last line of defence
SCBA, respirators, FR clothing, harness – always IN ADDITION to the above
MOST effective ↑ ↓ LEAST effective
Notes: TRAINER EXPLANATION: The hierarchy of controls tells us which controls to choose first. Always start at the top. Elimination removes the hazard completely. Substitution replaces it with something less hazardous. Engineering controls physically separate people from the hazard – isolation and LOTO are the primary domain of PTW. Administrative controls change how people work – the permit itself is one. PPE is the last line of defence and is always used in addition to the others, never instead of them. SIMPLE EXAMPLE: Need to cut a pipe in a gas plant? First ask: can the work wait until the unit is shut down and depressurised (elimination)? Can we use a hydraulic cutter instead of a grinder so there are no sparks (substitution)? Then isolate and ventilate (engineering), issue the permit and brief (administrative), and wear the right PPE. ASK THE TRAINEES: Why is relying only on PPE called 'a failure of the PTW process'? EXPECTED ANSWER: Because PPE does not eliminate the hazard; it only protects if it is the right type, worn correctly and does not fail. TRAINER REMINDER: The Permit Issuer should first ask: 'Can this hazard be eliminated?' ANIMATION: Each level wipes in from the top. SOURCE: Module 7 Course Notes – Section 5.3

## Slide 51: The Bow-Tie: Barriers on Both Sides
TOP EVENT
Release of flammable gas
PREVENT (left side)
MITIGATE (right side)
Isolation valve
Gas detection alarm
Positive blind
Fire watch
Lockout
Emergency Response Plan
The PTW must verify that ALL relevant barriers on BOTH sides are in place.
Notes: TRAINER EXPLANATION: The bow-tie is a simple picture for major hazards. In the middle is the top event – the moment control is lost. The example in the Course Notes is 'release of flammable gas'. On the left are preventive barriers that stop it happening: isolation valve, positive blind, lockout. On the right are mitigating barriers that limit the damage if it does happen: gas detection alarm, fire watch, emergency response plan. SIMPLE EXAMPLE: Before breaking a flange on a gas line, the Issuer checks the left side – valves locked, blind installed – AND the right side – gas monitor running, fire extinguisher ready, escape route clear. ASK THE TRAINEES: Is a fire watch a preventive or a mitigating barrier in this bow-tie? EXPECTED ANSWER: Mitigating – it limits consequences if the release happens. TRAINER REMINDER: The permit must verify barriers on BOTH sides. ANIMATION: Click 1 preventive barriers, click 2 mitigating barriers, click 3 key line. SOURCE: Module 7 Course Notes – Section 5.3.3

## Slide 52: JSA + PTW and Residual Risk
JSA
Planning & analysis tool
+
PTW
Authorisation & field verification
Inseparable. The Issuer reviews the JSA as a “second set of eyes” and turns it into explicit permit conditions.
Communicating residual risk in the briefing
“The major hazards we face are…” trapped pressure and flammable gas
“To control them we have…” locked the valves, installed the blind, tested the gas (point to them)
“The remaining risk is… so we will…” a minor leak at the final flange – crack it slowly from the top side, stand clear, gas monitor ready
Notes: TRAINER EXPLANATION: The JSA and the PTW work together. The JSA is the planning tool written by the work team; the PTW is the authorisation and field-verification tool. The Issuer does not blindly accept the JSA – they add system hazards and turn general words into exact permit conditions. And because no job is zero-risk, the Receiver must explain the remaining – residual – risk in the briefing using three simple statements. SIMPLE EXAMPLE: This flange example is straight from the Course Notes: 'the remaining risk is a minor leak when we break the final flange. Therefore, we will crack it slowly from the top side, stand clear, and have the gas monitor ready.' ASK THE TRAINEES: If conditions change during the job, what happens to the JSA? EXPECTED ANSWER: It becomes a 'living JSA': the permit is suspended, the JSA is reviewed for the new hazard, and the permit may be re-issued with new conditions. TRAINER REMINDER: Informed consent: by signing and attending the briefing, workers confirm they have been told the residual risks and controls. Without clear communication of residual risk, that consent is invalid. SOURCE: Module 7 Course Notes – Sections 5.4 and 5.5

## Slide 53
SECTION 7
Permit Conditions & Isolation (LOTO)
The rules of engagement – and the most critical technical control
Notes: TRAINER EXPLANATION: The heart of a permit is not the signature block – it is the conditions and controls written on it. And the most critical technical control is isolation. SOURCE: Module 7 Course Notes – Sections 6.1–6.3

## Slide 54: Conditions on Every Permit
Mandatory for ALL permit work
Competency: trained & authorised for your role
Fitness: no alcohol, drugs or impairing medication
Stop Work Authority: everyone, unconditionally
Site rules: smoking, speed, phones, seatbelts
Housekeeping: clean site, waste in correct bins
Tools & equipment: fit for purpose, inspected, tagged
Limits written on THIS permit
Scope & location + “NO work is authorised on…”
Validity: e.g. 08:00 – 16:30 (24-h clock)
People: e.g. max 4 in the party; max 2 inside V-205
Tools: e.g. hand tools and air-driven intrinsically safe wrench only
Stop triggers: e.g. wind above 25 km/h, or rain starts
Notes: TRAINER EXPLANATION: Some conditions apply to every permit, whatever the task: competency, fitness for work, stop work authority, site rules, housekeeping and fit-for-purpose tools. Other conditions are specific limits written on this particular permit: exact scope, validity, maximum number of people, allowed tools, and environmental stop triggers. These limits prevent 'scope creep' – a common cause of incidents. SIMPLE EXAMPLE: The examples on the right are from the Course Notes: a vessel V-205 permit allowing a maximum of 2 people inside at once, hand tools and an air-driven intrinsically safe impact wrench only, and stop work if wind exceeds 25 km/h or rain begins. ASK THE TRAINEES: Why might a permit say 'NO electrical grinders or heaters permitted'? EXPECTED ANSWER: To control the introduction of ignition sources or incompatible equipment. TRAINER REMINDER: Permit conditions are legally binding 'rules of engagement', not suggestions. The specific numbers come from YOUR permit. SOURCE: Module 7 Course Notes – Sections 6.1 and 6.2

## Slide 55: Isolation Methods – Most to Least Reliable
1
Physical disconnection / removal
Remove a pipe spool, pull a fuse, disconnect a coupling – the most positive method
2
Positive mechanical isolation
Spade / spectacle / paddle blind – tagged, number recorded on the permit
3
Double block & bleed (locked)
Two closed valves + open bleed between. NOT acceptable as primary isolation for hydrocarbons / highly hazardous chemicals unless company standards allow
4
Single valve with lockout
ONLY for non-hazardous utilities (plant air, cooling water) or as secondary isolation
Standard: a zero-energy state, secured by a personal lock and a danger tag.
Notes: TRAINER EXPLANATION: ISOLATION – simple meaning: separating the equipment from its energy or hazardous material so it cannot reach the worker. The Course Notes rank isolation methods from most to least reliable. Best: physically disconnect or remove a section. Next: a positive blind in a flange. Then double block and bleed – two locked valves with an open bleed between – but it is not acceptable as the primary isolation for hydrocarbons or highly hazardous chemicals unless company standards specifically allow it, because both valves could leak. Lowest: a single locked valve, only acceptable for non-hazardous utilities or as a secondary isolation. SIMPLE EXAMPLE: For maintenance on equipment that held process gas, a single closed valve is not enough. The isolation plan uses a blind or removes a spool so gas cannot pass, with every point locked and tagged. ASK THE TRAINEES: Is a single locked valve acceptable to isolate a process gas line for maintenance? EXPECTED ANSWER: No – a single valve is only acceptable for non-hazardous utilities or as a secondary isolation. TRAINER REMINDER: Every blind is tagged with a unique number recorded on the permit, and the Issuer/Receiver visually confirm its position (spectacle blind turned to the 'blind' side). ANIMATION: Methods wipe in from best to least reliable. SOURCE: Module 7 Course Notes – Section 6.3.2

## Slide 56: Lock-Out Tag-Out (LOTO) Protocol
One person · one lock
Personal locks
Every worker exposed to the hazard applies their OWN lock to the hasp. Group or supervisor locks are not enough.
Danger tags
Durable, weatherproof: name, department, date, reason, and “DO NOT OPERATE – MEN AT WORK”.
Isolation Certificate
Lists every isolation point, tag number and lock owner – attached to the permit.
Verify (VOI)
Positive test of zero energy: try-start the motor, zero pressure at the worksite. The final step before signing.
Notes: TRAINER EXPLANATION: LOTO means Lock-Out Tag-Out. Four elements. First, personal locks: every worker exposed to the hazard puts their own lock on the hasp – one person, one lock. Second, standard danger tags saying who, why and 'DO NOT OPERATE – MEN AT WORK'. Third, the Isolation Certificate – the master list of every isolation point and lock owner, attached to the permit. Fourth, Verification of Isolation: after locking and tagging, prove zero energy with a positive test. SIMPLE EXAMPLE: Before working on a process pump, the suction and discharge valves are closed and locked on a group hasp. Each mechanic adds a personal padlock. Then the Isolating Authority opens a bleed and confirms the gauge reads zero, and tries to start the motor – it must not run. ASK THE TRAINEES: Why is a supervisor's group lock not enough to protect you? EXPECTED ANSWER: Because personal protection requires YOUR lock – only you control its removal. The Course Notes state supervisory or group locks are insufficient for personal protection. TRAINER REMINDER: Auditors check that every lock is a personal safety lock – not a master lock, tool lock or zip-tie – and that each lock belongs to a worker present and listed. SOURCE: Module 7 Course Notes – Sections 6.3.3, 8.2.2, 13.4

## Slide 57: Plant Scenario: Breaking a Flange (Line Breaking)
SITUATION A technician must break a flange on a line that carried flammable gas and H₂S.
QUESTION Is closing one valve enough?
NO. A single valve is only for non-hazardous utilities or as secondary isolation.
Be ready (contingency): pre-fitted leak clamp or emergency blind, absorbent material and drip trays at the worksite; crew briefed on their use.
1
Isolation plan: blind / disconnect + lock & tag
2
Isolation Certificate attached
3
VOI: zero pressure confirmed
4
Gas test where required
5
Walkdown, sign, toolbox talk
6
Crack slowly from far side, stand clear, monitor ready
Notes: TRAINER EXPLANATION: Let us apply isolation to a real line-breaking job. The question: is closing one valve enough? Let trainees answer first. The Course Notes are clear: single-valve isolation is only acceptable for non-hazardous utilities or as a secondary isolation. For a hazardous process line we need positive isolation – a blind or physical disconnection – locked and tagged, recorded on the Isolation Certificate, and verified at zero pressure before the permit is signed. Gas testing is done where required, then the walkdown, signatures and briefing. When breaking, follow the residual-risk instruction: crack it slowly from the top or far side, stand clear, with the gas monitor ready. SIMPLE EXAMPLE: Why is this so important in a sour-gas service? A leaking valve can let gas – including H2S – reach the flange. The blind gives a physical barrier the valve cannot. ASK THE TRAINEES: What emergency equipment should already be at the flange before the last bolt is loosened? EXPECTED ANSWER: A pre-fitted leak clamp or emergency blind, absorbent materials and drip trays – and the crew briefed on their use. TRAINER REMINDER: The Break of Containment permit is the specific, highly controlled permit for the FIRST break into any process system – check which permit your site requires. ANIMATION: Click 1: answer; click 2: contingency; then the six steps. SOURCE: Module 7 Course Notes – Sections 2.8.2, 5.5.2, 6.3, 9.2.2

## Slide 58
SECTION 8
Gas Testing & Atmospheric Monitoring
What we test, the acceptable levels, and how often
Notes: TRAINER EXPLANATION: Atmospheric hazards are dynamic – they change. So gas testing is not a one-time event; it is a monitoring programme designed to detect changes before they become dangerous. SOURCE: Module 7 Course Notes – Section 6.4

## Slide 59: What Are We Testing For?
OXYGEN (O₂)
Too little = suffocation. Too much = greater fire risk.
19.5% – 23.5%
FLAMMABLES (LEL)
LEL = the lowest gas concentration in air that can ignite. We work far below it.
< 10% LEL
TOXIC GASES
e.g. Hydrogen Sulphide (H₂S), Carbon Monoxide (CO). Limits are site-specific.
H₂S < 10 ppm
CO < 35 ppm
STOP & EVACUATE if the monitor alarms: LEL > 10%, O₂ < 19.5% or > 23.5%, H₂S > 10 ppm
Notes: TRAINER EXPLANATION: We test for three things. Oxygen: the acceptable range is 19.5 to 23.5 percent – too little and people suffocate, too much and fire risk increases. Flammables, measured as % of the Lower Explosive Limit: LEL simple meaning – the lowest amount of gas in air that can ignite; the acceptable level is below 10% LEL. Toxic gases such as hydrogen sulphide and carbon monoxide: limits are site-specific; the Course Notes give typical examples of H2S below 10 ppm and CO below 35 ppm. SIMPLE EXAMPLE: Before work on equipment that previously contained sour gas, the tester checks O2, LEL and H2S. A reading of H2S above 10 ppm means stop and evacuate. ASK THE TRAINEES: What does 'ppm' mean? EXPECTED ANSWER: Parts per million – a way of measuring very small concentrations of a gas. TRAINER REMINDER: NOTE FOR TRAINER: The Course Notes' testing table (6.4.2) also lists 'action at 20%, evacuate at 40%+ LEL', but the abort criteria (6.6.2), trigger events (9.1.2) and hot-work rules (2.1.3) all require work to STOP at > 10% LEL. Teach the stricter > 10% stop rule and follow your site procedure. Always use the limits written on YOUR permit. SOURCE: Module 7 Course Notes – Sections 2.3.1, 6.4.2, 6.6.2, 9.1.2

## Slide 60: How Gas Testing is Done
Test · Record · Re-test
1 Check
Calibrated monitor; bump-test before each day’s use
2 Sample
Pump & hose; top, middle, bottom; every compartment
3 Order
O₂ → Flammables → Toxics
4 Record
Gas Test Certificate attached to the permit
Continuous monitoring: confined spaces, hot work in possibly flammable areas, or wherever conditions could change
Worn in the breathing zone or fixed near the work; visual, audible & vibrating alarms
Re-test: typically every 30–60 min in confined spaces, and before re-entry after any break
Notes: TRAINER EXPLANATION: Gas testing has a routine. Check the instrument: calibrated, and bump-tested – a quick function check – before each day's use. Sample with a pump and hose at the top, middle and bottom, because gases form layers, and test every compartment. Test in order: oxygen, then flammables, then toxics. Record every test on the Gas Test Certificate – location, time, tester, readings and instrument serial number – and attach it to the permit. SIMPLE EXAMPLE: For a vessel entry, the tester takes a baseline with the space open but not yet ventilated, then again after ventilation. During the job, the attendant monitors at the entrance and re-tests are recorded, typically every 30 to 60 minutes and before re-entry after a break. ASK THE TRAINEES: Why do we test at the top, middle AND bottom? EXPECTED ANSWER: Because of gas stratification – heavier gases settle low and lighter gases rise, so one reading may miss a hazard. TRAINER REMINDER: The tester must be a competent, authorised person. Falsifying a gas test certificate is a MAJOR non-conformance. SOURCE: Module 7 Course Notes – Sections 2.3.3, 6.4.2, 8.2.2, 11.3.2

## Slide 61: Plant Scenario: Gas Reading During Work
Maintenance is working on an exchanger that previously contained sour gas. The last time it was opened, H₂S scale was found.
The gas monitor now reads 5% LEL – below the alarm. Do we continue?
THINK FIRST… then click to reveal the answer
Before the job: History of H₂S scale → the Issuer specifies continuous monitoring with an H₂S-specific detector.
5% LEL = significant deviation. Below alarm but above zero: STOP work and secure the site.
Then: Notify the Issuer → joint re-assessment (new JSA, extra controls) → resume only when re-validated.
If the alarm sounds: Evacuate immediately – it is an emergency trigger.
Notes: TRAINER EXPLANATION: This scenario uses two real examples from the Course Notes. First, history matters: because H2S scale was found the last time this exchanger was opened, specific toxic gas monitoring is required. Second, the Course Notes give 'a gas monitor reads 5% LEL – below alarm but above zero' as an example of a SIGNIFICANT deviation. The response is to stop work, secure the site, notify the Issuer and jointly re-assess before anything restarts. SIMPLE EXAMPLE: Many people think 'it's below the alarm so it's fine'. The Course Notes say otherwise: gas is present that was not expected, so the safe envelope may be broken. ASK THE TRAINEES: Who decides whether the work can restart? EXPECTED ANSWER: The Permit Issuer and Receiver jointly, after re-assessment. If the change is substantial, the permit is cancelled and a new one is raised. TRAINER REMINDER: Any reading that shows conditions have changed means stop and re-assess. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 5.1.2 E, 5.4.2, 7.3.2 B

## Slide 62
SECTION 9
PPE & Emergency Preparedness
The last line of defence – and the plan if controls fail
Notes: TRAINER EXPLANATION: Every permit must answer: 'If our primary controls fail, what then?' This section covers PPE and emergency planning. SOURCE: Module 7 Course Notes – Sections 6.5, 6.6, 9.0

## Slide 63: PPE Matrix Example: Welding in a Confined Space
Body part | Hazard | Minimum PPE
Head | Impact, falling objects | Hard hat
Eyes / face | UV, flying particles | Auto-darkening welding helmet + safety glasses underneath
Hearing | Grinder noise | Earmuffs or plugs
Respiratory | Welding fumes, toxic gases | PAPR with suitable cartridge, OR supplied air for IDLH
Body | Molten metal, sparks | Flame-resistant coveralls, leather jacket & sleeves
Hands / feet | Heat, cuts, heavy objects | Insulated leather gloves; safety boots with metatarsal guards
Fall protection | Fall at entry point | Full body harness on retractable lifeline / tripod
Layering
Safety glasses UNDER the welding helmet
Task-specific
Welding gloves ≠ chemical gloves
Pre-use check
PPE integrity is the worker’s responsibility
Notes: TRAINER EXPLANATION: PPE is chosen from a task- and hazard-specific risk assessment, not tradition. The Course Notes show a sample PPE matrix for one combined task: welding inside a confined space. Every body part has a hazard and a minimum PPE item. Three key principles: layering – safety glasses go under the welding helmet; task-specific – welding gloves are not chemical gloves; and pre-use checks – the worker checks their own PPE before use. SIMPLE EXAMPLE: For a welder working inside a vessel: helmet plus glasses, PAPR or supplied air depending on the atmosphere, FR coveralls and leather jacket, insulated gloves, safety boots, and a harness connected to the tripod lifeline at the entry point. ASK THE TRAINEES: Why is the harness listed in the PPE matrix for a confined space job? EXPECTED ANSWER: For fall protection at the entry point and to allow non-entry rescue using the tripod/retrieval system. TRAINER REMINDER: The PPE matrix on YOUR permit is the instruction. PPE is always used in addition to higher-level controls. SOURCE: Module 7 Course Notes – Sections 5.3.2, 6.5

## Slide 64: Emergency Planning on Every Permit
WHEN to act (triggers)
Fire or explosion
Uncontrolled release (liquid, gas, vapour)
Gas monitor alarm
Collapse or equipment failure
Medical emergency
Site emergency alarm
First 60 seconds
SHOUT a warning
STOP all work (if safe)
EVACUATE – don’t gather tools
ASSIST only without significant personal risk
ACTIVATE the alarm
Know your way out
Primary & secondary escape routes – walked and clear
Worksite Assembly Point (WSAP) upwind & uphill for headcount
Plan for locked gates / hatches
Notes: TRAINER EXPLANATION: PTW emergency planning does not replace the site Emergency Response Plan – it tailors it to this job. The Issuer and Receiver must define three things. WHEN to act: the trigger events. WHAT to do in the first 60 seconds: shout, stop, evacuate, assist only if safe, and raise the alarm. And WHERE to go: escape routes physically walked during the walkdown, and a Worksite Assembly Point upwind and uphill for an immediate headcount. SIMPLE EXAMPLE: In a gas plant, check the windsock during the walkdown. If H2S or hydrocarbon is released, you move upwind and uphill to the worksite assembly point, then follow the site muster procedure. ASK THE TRAINEES: Why should the Worksite Assembly Point be upwind and uphill? EXPECTED ANSWER: So released gas or vapour is carried away from people; heavier gases also flow downhill. TRAINER REMINDER: These triggers are verbally repeated in every pre-job briefing. Do not stop to gather tools. SOURCE: Module 7 Course Notes – Sections 6.6.2, 9.1

## Slide 65: Contingency Plans by Activity
Hot work
Spark ignites insulation or oil
Fire watch attacks the small fire with the pre-positioned extinguisher; second person calls for help
Confined space
Gas monitor alarms (e.g. H₂S)
Attendant orders evacuation → non-entry rescue (tripod/winch) → calls rescue team. NEVER enters
Excavation
Cracking, sloughing, water seepage
Evacuate trench; no re-entry until a competent person declares it safe
Electrical
Worker electrocuted / arc flash
DO NOT TOUCH. De-energise at LOTO point, or use non-conductive rescue hook
Breaking containment
Leak when last bolt loosened
Re-tighten if safe or fit leak clamp; absorbents & drip trays ready
Notes: TRAINER EXPLANATION: Contingency plans are pre-planned actions to control a developing situation before it becomes a full emergency. Each permit type has its own. The middle column shows what could go wrong; the right column shows the planned response. And each one has a verification during issue: the extinguisher is charged, the rescue equipment is set up, the rescue hook is at the worksite, the leak clamp is ready. SIMPLE EXAMPLE: For a vessel entry in our plant, if the gas monitor alarms for H2S, the attendant immediately orders everyone out, starts non-entry rescue with the tripod and winch if someone cannot get out, and calls the dedicated rescue team – but never goes in. ASK THE TRAINEES: A colleague is in contact with a live electrical source. What must you NOT do? EXPECTED ANSWER: Do not touch the victim. First de-energise at the established LOTO point, or use a non-conductive rescue hook. TRAINER REMINDER: The equipment for each contingency must be checked at the worksite during the pre-issue walkdown. SOURCE: Module 7 Course Notes – Section 9.2.2

## Slide 66: Emergency Communication & Rescue
Rescue plan BEFORE entry
METHANE emergency message
M
My exact location
E
Exact nature of emergency
T
Type of help needed
H
Hazards present
A
Access route for responders
N
Number & condition of casualties
E
Emergency services already called?
“Call 911” is NOT a rescue plan
Rescue team designated, trained & on alert
Response time stated – no work if rescue unavailable
Equipment staged: tripod, harnesses, SCBA, blower, stretcher
Non-entry rescue FIRST
Notes: TRAINER EXPLANATION: Failed communication is a primary reason emergencies escalate. Each permit has a layered plan: primary communication is the site radio on a set channel with a clear emergency phrase; backup is a phone, air horn or whistle signal. When you call the control room, use METHANE so nothing is missed. For confined space and high-risk work, a written rescue plan must be ready BEFORE work begins. 'Call 911' – or calling the outside emergency services – is NOT a rescue plan. SIMPLE EXAMPLE: 'Emergency, Emergency, Emergency – Fire at Pump Alley 1' is the example emergency call in the Course Notes. A backup signal could be three long horn blasts = evacuate. ASK THE TRAINEES: What is always the first and preferred rescue option for a confined space? EXPECTED ANSWER: Non-entry rescue – using the retrieval system to pull the entrant out. Entry rescue is a last resort, by specially trained people with breathing apparatus. TRAINER REMINDER: Work must not proceed if rescue capability is unavailable or the response time is unacceptable for the hazard (e.g. H2S exposure). Drills: tabletop quarterly; worksite drills at least annually per high-risk permit type. ANIMATION: METHANE letters wipe in; then the rescue panel. SOURCE: Module 7 Course Notes – Sections 9.3, 9.4, 9.5

## Slide 67
SECTION 10
During the Work: Monitor, Change, Stop, Hand Over
Signing the permit is the START of active safety, not the end
Notes: TRAINER EXPLANATION: A permit is a snapshot in time. The real world changes. Monitoring and supervision keep the safe envelope intact until the job is done. SOURCE: Module 7 Course Notes – Section 7.0

## Slide 68: Who Checks the Worksite – and What They Look For
Permit Receiver
Continuous – on or next to the site
Permit Issuer
At least once per shift; more for high risk
Safety Officer
Unannounced, random, risk-based audits
Management (VFL)
Visible leadership tours – conversations
Inspection checklist
Permit posted, valid, all signatures?
Work exactly as described?
Isolations locked? Monitor on & safe? Fire watch alert? Ventilation running?
Correct PPE worn properly?
Area tidy, access & escape clear?
Workers alert, not rushed or tired?
Weather, lighting or conditions changed?
Notes: TRAINER EXPLANATION: Compliance cannot be assumed – it must be verified by looking. The Receiver supervises continuously. The Issuer checks at least once per permit validity period – for example once per shift – and more for high-risk work. The Safety Officer does unannounced audits, and managers do Visible Felt Leadership tours that focus on conversations. The checklist on the right is what any of them looks for. SIMPLE EXAMPLE: An Issuer walking past a flange job checks: permit posted and valid? Locks still on the hasp? Gas monitor running and reading zero? Is the crew only working on the flange named on the permit? ASK THE TRAINEES: Pick one item on the checklist that you could check yourself as a worker. EXPECTED ANSWER: Any – e.g. is my PPE correct, is the escape route clear, has the weather changed? Every worker maintains situational awareness. TRAINER REMINDER: Monitoring requires a 'guardian mindset' – active curiosity, relentless verification and the courage to intervene. SOURCE: Module 7 Course Notes – Section 7.1

## Slide 69: When Conditions Change – 3 Levels of Response
MINOR
Control still effective
Example: non-critical PPE damaged; identical replacement available
Receiver approves substitution, tells crew, may note on permit – work continues
SIGNIFICANT
Control compromised or new hazard
Examples: unexpected pipe found behind insulation; rain starts during outdoor electrical work; monitor reads 5% LEL
STOP → secure → notify Issuer → joint re-assessment → amend & revalidate, or cancel and raise a new permit
MAJOR
Emergency
Examples: major leak, fire, gas alarm, structural instability, medical emergency
Evacuate to muster point → activate ERP → permit is void → investigation afterwards
Notes: TRAINER EXPLANATION: Changes during work are normal – what matters is how we respond. The Course Notes define three levels. Minor: the control is still effective – for example, a non-critical PPE item is damaged and an identical replacement is available; the Receiver approves the swap and work continues. Significant: a control is compromised or a new hazard appears – stop immediately, make the site safe, notify the Issuer, and re-assess together. Major: an emergency – evacuate, activate the ERP, and the permit becomes void. SIMPLE EXAMPLE: During a pipe job, the crew removes insulation and finds a pipe that is not on the drawing. That is a significant deviation: stop, secure, call the Issuer. They may need a new JSA, extra isolation and an amended – or completely new – permit. ASK THE TRAINEES: Rain starts during outdoor electrical work. Which level is this? EXPECTED ANSWER: Significant – it is one of the Course Notes' own examples. Stop, secure, notify the Issuer and re-assess. TRAINER REMINDER: If the change is substantial, the original permit is CANCELLED and a new application starts. Amendments need clear notes and initials from both Issuer and Receiver. SOURCE: Module 7 Course Notes – Section 7.3

## Slide 70: Stop Work Authority & Permit Suspension
STOP WORK AUTHORITY
Who: ANY worker, any time – apprentice, contractor or visitor
How: say “STOP WORK” + the reason – “Stop work! I smell gas.”
Response: work stops at once. No debate, no ridicule, no repercussions
Formal suspension – 5 steps
1 Notify
Receiver tells the Issuer: work stopped, permit suspended
2 Secure
Tools down, equipment de-energised if possible, barricade
3 Document
Permit marked SUSPENDED – time, date, reason, initials
4 Investigate
Same permit after amendment, or a new permit?
5 Restart
Joint revalidation + NEW crew briefing; “WORK RESUMED” initialled
Notes: TRAINER EXPLANATION: Stop Work Authority is described as the most important authority in the PTW system – the emergency brake. Anyone can use it, any time, for any safety concern: the newest apprentice, a contractor, a visitor. Say 'STOP WORK' and the reason. Work stops immediately – no debate, no ridicule, no repercussions. Then the formal suspension follows five steps: notify, secure, document, investigate and restart only after joint revalidation and a new briefing. SIMPLE EXAMPLE: A young technician helping on a flange job smells gas and shouts 'Stop work! I smell gas.' Everyone stops. The Receiver secures the site and calls the Issuer. Even if it turns out to be nothing, the technician did exactly the right thing. ASK THE TRAINEES: After a stop, what must happen before the crew starts again? EXPECTED ANSWER: The Issuer and Receiver jointly revalidate the permit, a new briefing is held with the crew, and both initial and time-stamp the 'WORK RESUMED' section. TRAINER REMINDER: Investigate the CONDITION that caused the stop, not the person who stopped the work. Retaliation against SWA is a 'cardinal cultural sin'. A rising number of SWA uses is a positive sign. SOURCE: Module 7 Course Notes – Sections 7.4, 10.3.2

## Slide 71: Shift Change – Never Leave the Work Unattended
Receiver → Receiver
Walk the site together; face-to-face brief: work done & remaining, status of every control, issues & near misses; review the permit; incoming Receiver SIGNS the handover block
Issuer → Issuer
Permit log reviewed in the operations handover; high-risk permits & those near expiry highlighted; incoming Issuer takes responsibility for all permits in the area
New crew
FULL toolbox talk for the new crew, even if work is continuous. New members sign on. Never assume knowledge carries over.
THE GOLDEN RULE
If the incoming Receiver is not there to accept the handover, the outgoing Receiver cannot leave – work may need to be safely suspended.
Example handover line: “The blind is in at Flange F-205, confirmed at 08:00. The gas monitor has been stable at 0% LEL.”
Notes: TRAINER EXPLANATION: Shift change is one of the riskiest moments in PTW, because information can be lost. The Course Notes call the solution a 'three-party handshake': Receiver to Receiver at the worksite, Issuer to Issuer in the control room, and a full new briefing for the new crew. The incoming Receiver signs the permit's shift-handover block to accept responsibility. SIMPLE EXAMPLE: The handover example from the Course Notes: 'The blind is in at Flange F-205, confirmed at 08:00. The gas monitor has been stable at 0% LEL.' That is specific, factual and checkable. ASK THE TRAINEES: The night-shift Receiver has not arrived and the day Receiver's shift is over. What happens? EXPECTED ANSWER: The day Receiver cannot leave; the work may need to be safely suspended. Work must never be left unattended during a shift change. TRAINER REMINDER: The Permit Coordinator also hands over the permit log between shifts. SOURCE: Module 7 Course Notes – Sections 3.2.2, 7.2

## Slide 72: Plant Scenario: Conditions Change
During flange work on a gas line, the wind changes direction and a worker notices a gas smell.
What should happen now?
THINK FIRST… then click to reveal the answer
1 Stop: Anyone can call “STOP WORK! I smell gas.” Work stops immediately.
2 Secure & notify: Make the site safe; Receiver notifies the Issuer; permit SUSPENDED.
3 If the alarm sounds or a release is seen: Emergency – evacuate upwind/uphill to the WSAP and raise the alarm.
4 Restart only after: Joint re-assessment, revalidation and a new briefing – or a new permit.
Notes: TRAINER EXPLANATION: This scenario combines everything from Section 10. A gas smell is a change in conditions – and smelling gas is literally the example the Course Notes use for Stop Work Authority. Let trainees discuss, then reveal each step. SIMPLE EXAMPLE: Wind changes are also named in the Course Notes as a reason to revalidate a hot work permit and as an environmental condition the Issuer must consider. ASK THE TRAINEES: Is the permit still valid after the work is stopped? EXPECTED ANSWER: No – it is suspended. Work resumes only when the Issuer and Receiver jointly revalidate it, or a new permit is issued. TRAINER REMINDER: Uncontrolled release and gas monitor alarm are both emergency trigger events – no hesitation. ANIMATION: Each step appears on click. SOURCE: Module 7 Course Notes – Sections 7.3, 7.4, 9.1.2

## Slide 73
SECTION 11
Completing the Job: Extend, Cancel or Close
The formal end of the safe envelope
Notes: TRAINER EXPLANATION: Every permit ends in one of three ways: it is closed after normal completion, extended (revalidated) if the work continues, or cancelled if the work cannot start or will not resume. SOURCE: Module 7 Course Notes – Sections 4.6, 4.7, 8.5

## Slide 74: Three Ways a Permit Ends
CLOSURE
Normal completion
Final joint walkdown
Site clean; blinds removed; flanges re-bolted
Personal locks off only after Issuer confirms
Both sign; time recorded
Logged CLOSED; archived (often 3–5 yrs)
EXTENSION / REVALIDATION
Work continues beyond validity
Receiver asks BEFORE expiry
Fresh joint walkdown
Re-verify controls (fresh gas test, isolations)
Issuer signs new expiry
NEVER automatic
CANCELLATION
Work stopped or not started
Conditions changed before start
Work stopped – won’t resume on this permit
Significant scope / hazard change
Site made safe; both sign with reason
Archived as CANCELLED
Notes: TRAINER EXPLANATION: There are three ways a permit ends. Closure is the normal ending: a final joint walkdown, the site restored, locks removed only after the Issuer confirms, both sign, and the permit is logged closed and archived. Extension or revalidation is used when work must continue beyond the validity: the Receiver asks before expiry, and the Issuer repeats a fresh walkdown and re-verifies the controls – extensions are never automatic. Cancellation is used when work cannot start, stops and will not resume on this permit, or the scope or hazard changes significantly. SIMPLE EXAMPLE: A vessel inspection takes longer than one shift. Before the permit expires, the Receiver asks for revalidation. The Issuer walks the site again, a fresh gas test is done and the isolations are checked before the new expiry time is signed. ASK THE TRAINEES: The permit expired 10 minutes ago and the job is nearly finished. Can the team just finish quickly? EXPECTED ANSWER: No. Work must stop immediately if the permit expires, and can only resume after formal revalidation by the Issuer. TRAINER REMINDER: A cancelled permit is still archived – it remains part of the record and the audit trail. A high extension rate can indicate poor planning. SOURCE: Module 7 Course Notes – Sections 1.4.2, 4.7, 8.5, 10.3.2

## Slide 75: Closing a Permit – Step by Step
1 Finish
Receiver confirms all work done
2 Clean up
Tools, debris, slag removed; people out
3 Inform
Tell Issuer – locks still ON
4 Walk down
Joint final inspection; restoration verified
5 Unlock
Personal locks off only after Issuer OK
6 Sign & log
Both sign; CLOSED in log; archived
The Issuer’s closure signature is the legal moment when responsibility for the workspace returns from Maintenance to Operations.
Notes: TRAINER EXPLANATION: Closure is a formal process, not an afterthought. The Receiver confirms the work is complete, the area is cleaned and everyone is out – but the team's locks stay on. The Receiver tells the Issuer. Together they do a final walkdown and check restoration: temporary controls removed, blinds out, valves restored, equipment safe for return to service. Only then do workers remove their personal locks. Both sign the closure section with the time, and the Coordinator logs it as closed. SIMPLE EXAMPLE: After a pump seal change, the Issuer checks the blind at F-101 is removed and the flange is re-bolted before the mechanics take off their padlocks. Then the pump can be returned to Operations. ASK THE TRAINEES: Why must the team's personal locks stay on until after the Issuer's final inspection? EXPECTED ANSWER: So the equipment cannot be re-energised or returned to service until the Issuer has verified that the work is complete and the site is safe. TRAINER REMINDER: If an incident happened during the job, the permit is NOT closed or archived until released by the investigation team. ANIMATION: Steps wipe in; then the legal-moment banner. SOURCE: Module 7 Course Notes – Sections 4.6, 4.7.2 A, 8.5.2, 10.2.2

## Slide 76: Trainer Question: Job Done Early
The pump seal job finished at 15:30. The permit is valid until 16:30.
Can the team remove their locks and go home?
THINK FIRST… then click to reveal the answer
NO. Locks stay on. The Receiver informs the Issuer the site is ready for inspection and handback.
Next: Joint final walkdown – restoration verified (blind removed, flange re-bolted, area clean).
Then: Personal locks removed after Issuer’s OK; both sign closure; logged CLOSED.
Notes: TRAINER EXPLANATION: A simple but very common situation. The job is finished early – can the crew just pack up? Ask the group, then reveal. ASK THE TRAINEES: What could happen if the locks come off before the Issuer's inspection? EXPECTED ANSWER: The pump could be returned to service with a blind still installed or a flange not fully re-bolted – or re-energised while something is still open. TRAINER REMINDER: The Receiver's job ends with formally returning the permit – not with leaving the site. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 4.6.2, 4.7.2

## Slide 77
SECTION 12
Records, Audits & Competence
How the system proves itself – and keeps improving
Notes: TRAINER EXPLANATION: This section is short for beginners. It explains why paperwork matters, how the system is checked, and how people become authorised. SOURCE: Module 7 Course Notes – Sections 8.0, 10.0–13.0

## Slide 78: Good Permit Paperwork
What every permit contains
Number & type · exact location & description (with exclusions) · hazards & specific controls · PPE · emergency info · Issuer & Receiver signatures with times · validity, extension, handover & suspension blocks · closure section
Attached certificates
Isolation Certificate · Gas Test Certificate · Confined Space checklist & Attendant log · Fire Watch log · JSA · Method statement – same permit number
Rules
No blank fields – write N/A
Times in 24-h format, in logical order
Changes: single line, initial, date – no white-out
e-PTW? A printed copy is still posted at site
Common failures
Vague description – “work on pump”
Missing signatures, times or dates
Certificates missing or unsigned
Conditions changed by scribbling
No record of the pre-job briefing
Notes: TRAINER EXPLANATION: Documentation is the evidence of due diligence. Every permit has standard sections, and supporting certificates are attached with the same permit number – a certificate is invalid without its master permit, and vice versa. Simple rules: no blank fields – write N/A to show it was considered; use 24-hour times in logical order; correct mistakes with a single line, initials and date. With an electronic permit system, a printed copy is still posted at the worksite. SIMPLE EXAMPLE: An auditor picks a closed permit for a vessel entry. The gas test certificate has readings but no tester signature, and the shift-handover block is blank. Those are exactly the failures listed on the right. ASK THE TRAINEES: Why should you write 'N/A' rather than leave a field blank? EXPECTED ANSWER: To show the item was considered, not forgotten. TRAINER REMINDER: In any investigation, the permit dossier is 'Exhibit A'. Sloppy records are the hallmark of a sloppy safety process. SOURCE: Module 7 Course Notes – Sections 8.1–8.5

## Slide 79: Checking & Improving the System
3 lines of defence
1st: Issuers & Receivers – daily checks, walkdowns, handovers
2nd: HSE internal audits – system, field and trace audits
3rd: External – regulators, corporate, third party
Audit findings
MAJOR: e.g. work without a required permit; no isolation; falsified gas test; no briefing → STOP work
MINOR: e.g. permit not posted; missing non-critical signature
OFI: an idea to improve
After every job
What went well?
What surprised us?
What would we do differently?
Any system issues?
A near miss is a free lesson – report it.
Notes: TRAINER EXPLANATION: The PTW system checks itself. The first line of defence is the daily work of Issuers and Receivers. The second is HSE internal audits. The third is external assurance. Audit findings are classified: a major non-conformance means a critical breakdown that could lead directly to a serious incident – work stops; a minor one is a lapse that weakens the system; an Opportunity for Improvement is an idea. After every job, a short 4-point review captures lessons, and near misses are reported without blame. SIMPLE EXAMPLE: The Course Notes' root-cause example: a worker was found grinding without a Hot Work Permit. Asking 'why' five times showed the real cause – small reactive jobs were never planned – so the fix was a new procedure, not just blaming the worker. ASK THE TRAINEES: Is a rising number of Stop Work Authority uses good or bad news? EXPECTED ANSWER: Good news – the Course Notes say an increasing trend is positive because it shows people feel safe to speak up. TRAINER REMINDER: Post-work review: 10–15 minutes, ideally within 24 hours, focused on learning not blame. SOURCE: Module 7 Course Notes – Sections 10.1–10.3, 11.1–11.3

## Slide 80: Training & Competence – “Show Me, Don’t Tell Me”
TIER 1 General awareness
Everyone on site · 1–2 h
Purpose, Life Saving Rule, alarms, Stop Work Authority, how to recognise a permit
TIER 2 PTW user
Workers under permits · 4–8 h
Forms & certificates, roles, toolbox talks, reading a live permit, gas monitors
TIER 3 Role authorisation
Issuer, Receiver, Isolator, Attendant, Fire Watch · 16–40 h
Deep role skills + assessment + mentoring
TIER 4 Auditor & trainer
HSE, senior supervisors
Audit, root cause, training delivery
Competency is proven by observation · role & area specific · re-certified every 2–3 years · listed in the Competency Register
Notes: TRAINER EXPLANATION: Competency is described as the single most critical component of the PTW system. Training is tiered. Today's course covers Tier 1 awareness and the basis of Tier 2 user knowledge. People who will act as Issuers, Receivers, Isolating Authorities, Attendants or Fire Watches need Tier 3 role training and must be assessed – 'show me, don't tell me' – including direct observation on real jobs. Authorisations are role- and area-specific, recorded in the Competency Register and re-certified, typically every 2 to 3 years. SIMPLE EXAMPLE: A new Permit Issuer candidate must be observed issuing at least 3–5 permits of varying complexity under supervision before they are authorised to issue alone. ASK THE TRAINEES: Does attending a course make you an authorised Permit Receiver? EXPECTED ANSWER: No – competency must be proven through assessment, and authorisation is granted formally and recorded in the Competency Register. TRAINER REMINDER: Anyone issuing or receiving a permit must have an active status in the register for that role. SOURCE: Module 7 Course Notes – Sections 12.1–12.5

## Slide 81
SECTION 13
Practical Scenarios & Key Takeaways
Apply what you have learned to real plant situations
Notes: TRAINER EXPLANATION: Now we put it all together. Use these scenarios as group exercises – give teams two minutes per scenario before revealing the answers. SOURCE: Module 7 Course Notes – All sections

## Slide 82: Scenario: Entering a Process Vessel
A team must enter vessel V-205 in the gas plant for inspection. It previously contained process gas that may include H₂S.
What must be in place before and during entry?
THINK FIRST… then click to reveal the answer
Permit: Confined Space Entry permit/certificate + Isolation Certificate (combined under the master permit)
Isolate & prepare: Lock out all energy; blind/disconnect all piping; clean & purge; continuous forced ventilation
Gas test: O₂ → LEL → toxics (H₂S) at top, middle, bottom; results on the Gas Test Certificate
People: Entrant(s) – e.g. max 2 inside V-205; Attendant outside (never enters); Entry Supervisor
Rescue: Tripod, winch, harnesses, SCBA; rescue team on alert; non-entry rescue first
During: Continuous monitoring; re-test after breaks; 1 entry / max 4 h; suspend if conditions change
Notes: TRAINER EXPLANATION: Give the group two minutes to list everything needed for this vessel entry, then reveal the six answers. Everything comes from Sections 2.3, 6.2, 6.4 and 9.4 of the Course Notes. SIMPLE EXAMPLE: The Course Notes use V-205 itself as an example of a personnel limit: 'Maximum number of personnel inside the confined space (V-205) simultaneously: 2.' ASK THE TRAINEES: Why is natural ventilation not enough? EXPECTED ANSWER: The Course Notes require continuous forced mechanical ventilation from a clean air source – natural ventilation is insufficient for confined spaces. TRAINER REMINDER: Oxygen deficiency and H2S are both atmospheric hazards that cannot be seen. The attendant monitors at the entrance throughout; work must not proceed if rescue capability is unavailable. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 2.3, 6.2.2, 6.4, 9.4

## Slide 83: Scenario: Hot Work Near Operating Equipment
Maintenance wants to weld a support near operating gas-treatment equipment. Production pressure is high – “just start, we’ll do the permit after.”
What must happen?
THINK FIRST… then click to reveal the answer
Stop: No valid Hot Work Permit = Life Saving Rule breach. Use Stop Work Authority.
Plan: Can it be eliminated or substituted (e.g. hydraulic cutter, workshop)? JSA; SIMOPS check with nearby operations.
Control: Continuous gas monitoring (stop > 10% LEL); combustibles cleared/covered 15 m; openings covered.
Fire readiness: Dedicated fire watch with 9 kg extinguisher + radio, during and 60 min after; extinguishers & hose ready.
Forbidden if: Hazardous transfers, active hydrocarbon releases, or unsafe gas test.
Validity: One shift (max 12 h); revalidate after breaks or changes such as wind.
Notes: TRAINER EXPLANATION: This scenario combines the Life Saving Rule with hot-work controls. Let the group spot the problem first: 'we'll do the permit after' is a verbal authorisation and is not valid. SIMPLE EXAMPLE: The Course Notes' corrective-action example is almost identical: a worker found grinding without a Hot Work Permit because the supervisor was under pressure to finish before shift end. ASK THE TRAINEES: Who should check for conflicts with the operating equipment nearby? EXPECTED ANSWER: The Permit Issuer, with the Permit Coordinator flagging SIMOPS conflicts – the Issuer considers adjacent operations, utilities and environmental conditions. TRAINER REMINDER: Leadership must show that no production or schedule pressure justifies bypassing the PTW process. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 1.4, 2.1, 3.1.2, 4.2.2, 11.3.3

## Slide 84: Common PTW Mistakes – and the Right Way
MISTAKE
RIGHT WAY
Treating the permit as a tick-box
Walk, check and verify on site before signing
Verbal “go ahead”
Only a signed, valid permit authorises work
Vague scope: “work on pump”
Exact tag, location and exclusions
One valve for a hazardous line
Positive isolation, locked, tagged, VOI
Skipping or rushing the briefing
TRAHC toolbox talk with every worker
Working past expiry or scope
Stop, request revalidation or new permit
Leaving at shift change
Face-to-face handover; never unattended
Locks off before final inspection
Issuer’s walkdown first, then unlock
Notes: TRAINER EXPLANATION: This slide pulls together the most common mistakes described across the Course Notes – each paired with the right way. Reveal them one at a time and ask trainees whether they have seen any of them on site. SIMPLE EXAMPLE: The list mixes documentation failures (vague descriptions, missing briefing records), audit non-conformances (work without a permit, no isolation) and procedure rules (locks stay on until final inspection; never leave work unattended at shift change). ASK THE TRAINEES: Which of these mistakes do you think happens most often – and why? EXPECTED ANSWER: Open discussion. The Course Notes list underlying causes such as time pressure, unplanned reactive work and cumbersome processes – investigate the cause, not just the person. TRAINER REMINDER: Keep the discussion blame-free; the aim is learning. ANIMATION: Each pair appears on click. SOURCE: Module 7 Course Notes – Sections 1.2.1, 1.4.2, 6.3.2, 7.2.2, 8.4.3, 11.3.2

## Slide 85
10 PTW Golden Rules to Remember
1
No valid permit = no work
2
Know your permit: what, where, when, who
3
Hazards found, controls VERIFIED on site
4
Positive isolation, personal lock, VOI
5
Test the air – O₂, LEL, toxics
6
Brief every worker (TRAHC)
7
Stay inside the permit scope
8
Anything changes → STOP & tell the Issuer
9
Hand over face-to-face at shift change
10
Close formally – locks off last
Notes: TRAINER EXPLANATION: Ten golden rules to take away, each one taken from the Course Notes. Read them out one at a time, and ask the group to give a one-sentence reason for each. ASK THE TRAINEES: Which rule would have prevented the 'grinding without a permit' example we discussed? EXPECTED ANSWER: Rule 1 – no valid permit, no work (the Life Saving Rule) – supported by Rule 8 and Stop Work Authority. TRAINER REMINDER: These are memory aids. The detailed requirements are on your site's permit forms and procedure. ANIMATION: Each rule appears on click. SOURCE: Module 7 Course Notes – Sections 1.3, 1.4, 4.0–4.7, 6.3, 6.4, 7.2–7.4

## Slide 86: Final Quick-Fire Quiz
Answer out loud – then click to check.
Test yourself!
THINK FIRST… then click to reveal the answer
What is the Life Saving Rule? No work without a valid permit where a permit is required
Gas test order? Oxygen → Flammables → Toxics
Who signs first? The Permit Issuer – after verifying the site
What is VOI? Verification of Isolation – prove zero energy
Fire watch after hot work? At least 60 minutes
Who can stop work? Everyone – any time
Notes: TRAINER EXPLANATION: Use this quiz to close the course. Ask each question to a different trainee. TRAINER REMINDER: If several answers are weak, revisit that section briefly before closing. ANIMATION: Each answer appears on click. SOURCE: Module 7 Course Notes – Sections 1.4, 2.1, 2.3, 4.3, 6.3, 7.4

## Slide 87
Sending everyone home safely
A permit is a safety process – plan it, verify it, communicate it, follow it, close it.
Questions?
Notes: TRAINER EXPLANATION: The Course Notes end their roles section with one shared goal: sending everyone home safely. That is what PTW is for. Thank the group and open the floor for questions. TRAINER REMINDER: Collect feedback – the Course Notes encourage frontline feedback to improve the PTW process. SOURCE: Module 7 Course Notes – Section 3.8 Conclusion, 10.4

## Slide 88: Glossary – Key Terms in Simple Words
PTW | Permit to Work – formal written system to control high-risk work | ppm | Parts per million – unit for small gas concentrations
JSA / TRA | Job Safety Analysis / Task Risk Assessment – job steps, hazards, controls | SIMOPS | Simultaneous Operations – conflicting activities close together
LOTO | Lock-Out Tag-Out – locking and tagging isolation points | SWA | Stop Work Authority – everyone’s right to stop unsafe work
VOI | Verification of Isolation – test that proves zero energy | ALARP | As Low As Reasonably Practicable
DBB | Double Block & Bleed – two closed valves with an open bleed between | WSAP | Worksite Assembly Point – first muster for headcount
LEL | Lower Explosive Limit – lowest gas level in air that can ignite | MOC | Management of Change
H₂S | Hydrogen sulphide – a toxic gas | SCBA | Self-Contained Breathing Apparatus
Notes: TRAINER EXPLANATION: A reference slide with the key terms used today, in simple words. Leave it on screen during breaks or print it as a handout. SOURCE: Module 7 Course Notes – Section 14.0 Abbreviations